## Slide 1: Pervasive Idea: Abstraction and Layering
Abstraction: only way of dealing with complex systems
  Divide world into objects, each with an…
    Interface: knobs, behaviors, knobs  behaviors
    Implementation: “black box” (ignorance+apathy)
  Only specialists deal with implementation, rest of us with interface
  Example: only mechanics know how cars work
Layering: abstraction discipline makes life even simpler
  Divide objects in system into layers, layer n objects…
    Implemented using interfaces of layer n – 1
    (mostly) Don’t need to know interfaces of layer n – 2
Inertia: a dark side of layering
  Layer interfaces become entrenched over time (“standards”)
  Very difficult to change even if benefit is clear
Opacity: hard to reason about performance across layers
Notes: Feb 17, 2009: digital TV conversion date, was postponed to June 12th, even after significant government subsidy

## Slide 2: Abstraction, Layering, and Computers
Computers are complex, built in layers
  Several software layers: assembler, compiler, OS, applications
  Instruction set architecture (ISA)
  Several hardware layers: transistors, gates, CPU/Memory/IO
99% of users don’t know hardware layers implementation
90% of users don’t know implementation of any layer
  That’s okay, world still works just fine
  But sometimes it is helpful to understand what’s “under the hood”
CPU
Hardware
Software
ISA
Mem
I/O
System software
App
App
App
Transistors

## Slide 3: Why Study Hardware?
Understand where computers are going
  Future capabilities drive the (computing) world
  Real world-impact: no computer architecture  no computers!
Understand high-level design concepts
  The best system designers understand all the levels
    Hardware, compiler, operating system, applications
Understand computer performance
  Writing well-tuned (fast) software requires knowledge of hardware
Write better software
  The best software designers also understand hardware
  Understand the underlying hardware and its limitations
Design hardware
  Intel, AMD, IBM, ARM, Qualcomm, Apple, Oracle, NVIDIA, Samsung, …
Notes: Some of you will actually be designing chips and systems and working with things at this level
All of you will be writing code and if you know how the system works you will be able to take better advantage of things that the system does well and avoid things that the computer does poorly.
This understanding can have profound effects of code performance.

## Slide 4: Penn Legacy
ENIAC: electronic numerical integrator and calculator
  First operational general-purpose stored-program computer
  Designed and built here by Eckert and Mauchly
  See it in Moore 100!
First seminars on computer design
  Moore School Lectures, 1946
  “Theory and Techniques for Design of Electronic Digital Computers”

## Slide 5: What is Computer Architecture?

## Slide 6: Computer Architecture
Computer architecture
  Definition of ISA to facilitate implementation of software layers
  The hardware/software interface
Computer micro-architecture
  Design processor, memory, I/O to implement ISA
  Efficiently implementing the interface
CIS 371/501 is mostly about processor micro-architecture
  “architecture” is also a vacuous term for “the design of things”
    software architect, network architecture, …

## Slide 7: Application Specific Designs
This class is about general-purpose CPUs
  Processor that can do anything, run a full OS, etc.
  E.g., Intel Atom/Core/Xeon, AMD Ryzen/EPYC, ARM M/A series
In contrast to application-specific chips
  Or ASICs (Application specific integrated circuits)
    Also application-domain specific processors
  Implement critical domain-specific functionality in hardware
    Examples: video encoding, 3D graphics, machine learning
  General rules
    Hardware is less flexible than software
    Hardware more effective (speed, power, cost) than software
    Domain specific more “parallel” than general purpose
      But mainstream processors are quite parallel as well

## Slide 8: Technology Trends

## Slide 9: “Technology”
Basic element
  Solid-state transistor (i.e., electrical switch)
  Building block of integrated circuits (ICs)
What’s so great about ICs? Everything
  High performance, high reliability, low cost, low power
  Lever of mass production
Several kinds of integrated circuit families
  SRAM/logic: optimized for speed (used for processors)
  DRAM: optimized for density, cost, power (used for memory)
  Flash: optimized for density, cost (used for storage)
  Increasing opportunities for integrating multiple technologies
Non-transistor storage and inter-connection technologies
  Magnetic disks, optical storage, ethernet, fiber optics, wireless
channel
source
drain
gate

## Slide 10: Moore’s Law - 1965
Today: 233 transistors

## Slide 11: Moore’s Law today
data c/o WikiChip
Notes: gray line is Moore’s Law, doubling density every ~2.5 years
TSMC 7nm was used for Apple A12 processor, in iPhone XS/XR

## Slide 12: Moore’s Law today
data c/o WikiChip
Notes: gray line is Moore’s Law, doubling density every ~2.5 years
TSMC 7nm was used for Apple A12 processor, in iPhone XS/XR

## Slide 13: Revolution I: The Microprocessor
Microprocessor revolution
  One significant technology threshold was crossed in 1970s
  Enough transistors (~25K) to put a 16-bit processor on one chip
  Huge performance advantages: fewer slow chip-crossings
  Even bigger cost advantages: one “stamped-out” component
Microprocessors have allowed new market segments
  Desktops, CD/DVD players, laptops, game consoles, set-top boxes, mobile phones, digital camera, mp3 players, GPS, automotive
And replaced incumbents in existing segments
  Microprocessor-based system replaced supercomputers, “mainframes”, “minicomputers”, “desktops”, etc.

## Slide 14: First Microprocessor
Intel 4004 (1971)
  Application: calculators
  Technology: 10,000 nm
  2300 transistors
  13 mm2
  108 KHz
  12 Volts
  4-bit data
  Single-cycle datapath
Notes: 10um

## Slide 15: Revolution II: Implicit Parallelism
Then to extract implicit instruction-level parallelism
  Hardware provides parallel resources, figures out how to use them
  Software is oblivious
Initially using pipelining …
  Which also enabled increased clock frequency
… caches …
  Which became necessary as processor clock frequency increased
… and integrated floating-point
Then deeper pipelines and branch speculation
Then multiple instructions per cycle (superscalar)
Then dynamic scheduling (out-of-order execution)
We will talk about these things

## Slide 16: Pinnacle of Single-Core Microprocessors
Intel Pentium4 (2003)
  Application: desktop/server
  Technology: 90nm (1/100x)
  55M transistors (20,000x)
  101 mm2 (10x)
  3.4 GHz (10,000x)
  1.2 Volts (1/10x)
  32/64-bit data (16x)
  22-stage pipelined datapath
  3 instructions per cycle (superscalar)
  Two levels of on-chip cache
  data-parallel vector (SIMD) instructions, hyperthreading

## Slide 17: Revolution III: Explicit Parallelism
Then to support explicit data & thread level parallelism
  Hardware provides parallel resources, software specifies usage
  Why? diminishing returns on instruction-level-parallelism
First using (subword) vector instructions…, Intel’s SSE
  One instruction does four parallel multiplies
… and general support for multi-threaded programs
  Coherent caches, hardware synchronization primitives
Then using support for multiple concurrent threads on chip
  First with single-core multi-threading, now with multi-core
Graphics processing units (GPUs) are highly parallel
  Converging with general-purpose processors (CPUs)?

## Slide 18: Modern Multicore Processor
Intel Xeon E5-2699 V4 (2016)
  Application: server
  Technology: 14nm (16% of P4)
  7.2B transistors (130x)
  456 mm2 (4.5x)
  2.4 to 3.6 Ghz (~1x)
  1.8 Volts (~1x)
  256-bit data (2x)
  14-stage pipelined datapath (0.5x)
  4 instructions per cycle (1x)
  Three levels of on-chip cache
  data-parallel vector (SIMD) instructions, hyperthreading
  22-core multicore (22x)

## Slide 19: Revolution IV: Heterogeneous Processing
Combining multiple kinds of compute engines in one die
  not just homogenous collection of cores
  System-on-Chip (SoC) is one common example in mobile space
Lots of stuff on the chip beyond just CPUs
  Graphics Processing Units (GPUs)
    throughput-oriented specialized multicore processors
    good for gaming, machine learning, computer vision, …
  Special-purpose logic
    media codecs, radios, encryption, compression, machine learning
Excellent energy efficiency and performance
  extremely complicated to program!

## Slide 20
c/o Qualcomm

## Slide 21: Our lowly Zedboard FPGA

## Slide 22: Cerebras: Wafer-Scale Engine
giant 8.5” square chip!
full of deep learning accelerators
18GB on-chip memory
9 PB/sec on-chip memory bandwidth
TSMC 16nm transistors

## Slide 23: Technology Disruptions
Classic examples:
  The transistor
  Microprocessor
More recent examples:
    Flash-based solid-state storage
    Accelerators
Nascent disruptive technologies:
  non-volatile memory (“disks” as fast as DRAM)
  Chip stacking (also called 3D die stacking)
Disruptive “end-of-scaling”
  “If something can’t go on forever, it must stop eventually”
  Transistor speed/energy efficiency not improving like before

## Slide 24: Themes
Parallelism
  How do we enhance system performance by doing multiple things at once.
  This happens at multiple levels: Instruction Level Parallelism, multicore, GPU
How do we accelerate access to data
  Exploiting locality of reference, building storage hierarchies and caches
  Try to provide the illusion of a single large, fast memory