## Slide 1: Transistors & Fabrication

## Slide 2
Intel Pentium M Wafer

## Slide 3: Semiconductor Technology
Basic technology element: MOSFET
  Solid-state component acts like electrical switch
  MOS: metal-oxide-semiconductor
    Conductor, insulator, semi-conductor
FET: field-effect transistor
  Channel conducts sourcedrain only when voltage applied to gate
Channel length: characteristic parameter (short  fast)
  Aka “feature size” or “technology”
  Currently: 0.007 micron (mm), 7 nanometers (nm)
  Continued miniaturization (scaling) known as “Moore’s Law”
    Won’t last forever, physical limits approaching (or are they?)
channel
source
drain
insulator
gate
Substrate
channel
source
drain
gate

## Slide 4: Complementary MOS (CMOS)
Voltages as values
  Power (VDD) = “1”, Ground = “0”
Two kinds of MOSFETs
  N-transistors
    Conduct when gate voltage is 1
    Good at passing 0s
  P-transistors
    Conduct when gate voltage is 0
    Good at passing 1s
CMOS
  Complementary n-/p- networks form boolean logic (i.e., gates)
  And some non-gate elements too (important example: RAMs)
power (1)
ground (0)
input
output
(“node”)
n-transistor
p-transistor

## Slide 5: Basic CMOS Logic Gate
Inverter: NOT gate
  One p-transistor, one n-transistor
  Basic operation
  Input = 0
    P-transistor closed, n-transistor open
    Power charges output (1)
  Input = 1
    P-transistor open, n-transistor closed
    Output discharges to ground (0)
0
1
1
0

## Slide 6: Another CMOS Gate Example
What is this? Look at truth table
  0, 0  1
  0, 1  1
  1, 0  1
  1, 1  0
  Result: NAND (NOT AND)
  NAND is “universal”
  What function is this?
B
A
A
B
output
B
A
A
B
output
Notes: NOR – Not Or

## Slide 7: Digital Building Blocks: Logic Gates
Logic gates: implement Boolean functions
  Basic gates: NOT, NAND, NOR
    Underlying CMOS transistors are naturally inverting ( = NOT)
  NAND, NOR are “Boolean complete”
NAND
NOR
XOR
NOT (Inverter)
A
A’
A
B
(AB)’
(A+B)’
A
B
BUF
OR
AND
ANDNOT
AND3
A
A
A
B
A
B
A
B
A
B
A
B
C
AB
AB’
AB’+A’B
(A^B)
A+B

## Slide 8: Digital Logic Review

## Slide 9: Boolean Functions and Truth Tables
Any Boolean function can be represented as a truth table
  Truth table: point-wise input  output mapping
  Function is disjunction of all rows in which “Out” is 1
  A,B,C  Out
  0,0,0  0
  0,0,1  0
  0,1,0  0
  0,1,1  0
  1,0,0  0
  1,0,1  1
  1,1,0  1
  1,1,1  1
  Example above: Out = AB’C + ABC’ + ABC
Notes: We will return to this when we talk about CLBs in FPGAs

## Slide 10: Truth Tables and PLAs
Implement Boolean function by implementing its truth table
  Takes two levels of logic
    Assumes inputs and inverses of inputs are available (usually are)
  First level: ANDs (product terms)
  Second level: ORs (sums of product terms)
PLA (programmable logic array)
  Flexible circuit for doing this

## Slide 11: PLA Example
PLA with 3 inputs, 2 outputs, and 4 product terms
  Out0 = AB’C + ABC’ + ABC
A
B
C
Out0
Out1
Permanent connections
Programmable connections (unconnected)
Notes: One implementation with a programmable interconnect.

## Slide 12: Boolean Algebra
Boolean Algebra: rules for rewriting Boolean functions
  Useful for simplifying Boolean functions
    Simplifying = reducing gate count, reducing gate “levels”
  Rules: similar to logic (0/1 = F/T)
    Identity: A1 = A, A+0 = A
    0/1: A0 = 0, A+1 = 1
    Inverses: (A’)’ = A
    Idempotency: AA = A, A+A = A
    Tautology: AA’ = 0, A+A’ = 1
    Commutativity: AB = BA, A+B = B+A
    Associativity: A(BC) = (AB)C, A+(B+C) = (A+B)+C
    Distributivity: A(B+C) = AB+AC, A+(BC) = (A+B)(A+C)
    DeMorgan’s: (AB)’ = A’+B’, (A+B)’ = A’B’

## Slide 13: Logic Minimization
Logic minimization
  Iterative application of rules to reduce function to simplest form
  Design tools do this automatically
    Out = AB’C + ABC’ + ABC
    Out = A(B’C + BC’ + BC) // distributivity
    Out = A(B’C + (BC’ + BC)) // associativity
    Out = A(B’C + B(C’+C)) // distributivity (on B)
    Out = A(B’C + B1) // tautology
    Out = A(B’C + B) // 0/1
    Out = A((B’+B)(C+B)) // distributivity (on +B)
    Out = A(1(B+C)) // tautology
    Out = A(B+C) // 0/1

## Slide 14: Non-Arbitrary Boolean Functions
PLAs implement Boolean functions point-wise
  E.g., represent f(X) = X+5 as [05, 16, 27, 38, …]
  Mainly useful for “arbitrary” functions, no compact representation
Many useful Boolean functions are not arbitrary
  Have a compact implementation
  Examples
    Multiplexer
    Adder

## Slide 15: Multiplexer (Mux)
Multiplexer (mux): selects output from N inputs
  Example: 1-bit 4-to-1 mux
  Not shown: N-bit 4-to-1 mux = N 1-bit 4-to-1 muxes + 1 decoder
A
O
B
C
D
S (binary)
S (binary)
A
B
C
D
O
S (1-hot)

## Slide 16: Adder
Adder: adds/subtracts two binary integers in two’s complement format
  Half adder: adds two 1-bit “integers”, no carry-in
  Full adder: adds three 1-bit “integers”, includes carry-in
  Ripple-carry adder: N chained full adders add 2 N-bit integers
  To subtract: negate B input, set bit 0 carry-in to 1

## Slide 17: Full Adder
What is the logic for a full adder?
  Look at truth table
    CI A B  C0 S
    0 0 0  0 0
    0 0 1  0 1
    0 1 0  0 1
    0 1 1  1 0
    1 0 0  0 1
    1 0 1  1 0
    1 1 0  1 0
    1 1 1  1 1
  S = C’A’B + C’AB’ + CA’B’ + CAB = C ^ A ^ B
  CO = C’AB + CA’B + CAB’ + CAB = CA + CB + AB
FA
B
S
CO
A
CI
A
B
S
CI
CO

## Slide 18: N-bit Adder/Subtracter
S
+/-
FA
B1
S1
A1
FA
B0
S0
A0
FA
BN-1
SN-1
AN-1
1
…
0
+/–
+/–
B
A
More later when we cover arithmetic

## Slide 19: FPGAs

## Slide 20: Alternative to Fabrication: FPGA
We’ll use FPGAs (Field Programmable Gate Array)
  Also called Programmable Logic Devices (PLDs)
An FPGA is a special type of programmable chip
  Conceptually, contains a grid of gates
  The wiring connecting them can be reconfigured electrically
    Using more transistors as switches
  Once configured, the FPGA can emulate any digital logic design
  Tool converts gate-level design to configuration
Uses
  Hardware prototyping (what “we” are doing)
  Low-volume special-purpose hardware
  Network processing. FPGAs in AWS, Azure Clouds

## Slide 21: FPGA
A Field Programmable Gate Array contains a collection of configurable logic elements and a programmable interconnect that can be set up to perform the desired logical operations.

## Slide 22: Configurable Logic Blocks
Each of the configurable logic blocks (or logic cells) contains some lookup tables and one or more flip-flops.
By setting the entries in the lookup tables (LUTs) these units can be programmed to implement arbitrary logical functions on their inputs.
http://en.wikipedia.org/wiki/Field-programmable_gate_array
ZedBoard has 85K logic cells
Notes: walkthrough LUT-as-gate

## Slide 23: Configuring FPGAs
By configuring the CLBs and the interconnect the FPGA can be ‘programmed’ to implement the desired operation.

## Slide 24: Hardware Design Methods

## Slide 25: Hardware Design Methodologies
Fabricating a chip requires a detailed layout
  All transistors & wires
How does a hardware designer describe such design?
  (Bad) Option #1: draw all the masks “by hand”
    All 1 billion transistors? Umm…
  Option #2: use computer-aided design (CAD) tools to help
    Layout done by engineers with CAD tools or automatically
Design levels – uses abstraction
  Transistor-level design – designer specifies transistors (not layout)
  Gate-level design – designer specifics gates, wires (not transistors)
  Higher-level design – designer uses higher-level building blocks
    Adders, memories, etc.
    Or logic in terms of and/or/not, and tools translates into gates

## Slide 26: Describing Hardware
Two general options
Schematics
  Pictures of gates & wires
Hardware description languages
  Use textual descriptions to specify hardware
Translation process called “synthesis”
  Textual description -> gates -> full layout
    Tries to minimizes the delay and/or number of gates
  Much like process of compilation of software
    Much slower!

## Slide 27: Schematics
Draw pictures
  Use a schematic entry program to draw wires, logic blocks, gates
  Support hierarchical design (arbitrary nesting)
  Good match for hardware which is inherently spatial
  Time consuming, “non-scalable” (large designs are unreadable)
  Rarely used in practice (“real-world” designs are too big)
S
O
B
A

## Slide 28: Hardware Description Languages (HDLs)
Write “code” to describe hardware
  HDL vs. SDL
  Specify wires, gates, modules (also hierarchical)
  Easier to create, edit, modify, scales well
  Misleading “sequential” representation: must still “think” spatially (gets easier with practice)
  module mux2to1(S, A, B, Out);
  input S, A, B;
  output Out;
  wire S_, AnS_, BnS;
  not (S_, S);
  and (AnS_, A, S_);
  and (BnS, B, S);
  or (Out, AnS_, BnS);
  endmodule
S
Out
B
A

## Slide 29: (Hierarchical) HDL Example
Build up more complex modules using simpler modules
  Example: 4-bit wide mux from four 1-bit muxes
  module mux2to1_4(S, A, B, Out);
  input [3:0] A;
  input [3:0] B;
  input S;
  output [3:0] Out;
  mux2to1 mux0 (S, A[0], B[0], Out[0]);
  mux2to1 mux1 (S, A[1], B[1], Out[1]);
  mux2to1 mux2 (S, A[2], B[2], Out[2]);
  mux2to1 mux3 (S, A[3], B[3], Out[3]);
  endmodule
S
4
4
4
A
B
Out
Notes: Key point – abstraction of designs.

## Slide 30: Verilog HDL
Verilog: HDL we will be using
  Syntactically similar to C (by design)
  Ease of syntax hides fact that this isn’t C (or any software lang)
  We will use a few lectures to learn Verilog
  module mux2to1_4(S, A, B, Out);
  input [3:0] A;
  input [3:0] B;
  input S;
  output [3:0] Out;
  mux2to1 mux0 (S, A[0], B[0], Out[0]);
  mux2to1 mux1 (S, A[1], B[1], Out[1]);
  mux2to1 mux2 (S, A[2], B[2], Out[2]);
  mux2to1 mux3 (S, A[3], B[3], Out[3]);
  endmodule
These aren’t variables
These aren’t function calls

## Slide 31: HDLs are not “SDLs”
SDL == Software Description Language (e.g., Java, C)
Similar in some (intentional) ways …
  Syntax
    Named entities, constants, scoping, etc.
  Tool chain: synthesis tool analogous to compiler
    Multiple levels of representation
    “Optimization”
    Multiple targets (portability)
  “Software” engineering
    Modular structure and parameterization
    Libraries and code repositories
… but different in many others
  One of the most difficult conceptual leaps of this course

## Slide 32: Hardware is not Software
Just two different beasts (or two parts of the same beast)
  Things that make sense in hardware, don’t in software, vice versa
  One of the main themes of this course
Software is sequential
  Hardware is inherently parallel and “always on”
  Have to work to get hardware to not do things in parallel
Software atoms are purely functional (“digital”)
  Hardware atoms have quantitative (“analog”) properties too
  Including correctness properties!
Software mostly about quality (“functionality”)
  Hardware mostly about quantity: performance, area, power, etc.
One reason that HDLs are not SDLs
Notes: Tip write Verilog but think in terms of schematics.

## Slide 33: HDL: Behavioral Constructs
HDLs have low-level structural constructs
  Specify hardware structures directly
  Transistors, gates (and, not) and wires, hierarchy via modules
Also have mid-level behavioral constructs
  Specify operations, not hardware to perform them
  Low-to-medium-level: &, ~, +, *
Also higher-level behavioral constructs
  High-level: if-then-else, for loops
  Some of these are synthesizable (some are not)
    Tools try to guess what you want, often highly inefficient
    Higher-level  more difficult to know what it will synthesize to!
HDLs are both high- and low-level languages in one!
  And the boundary is not clear!

## Slide 34: HDL: Simulation
Another use of HDL: simulating & testing a hardware design
  Cheaper & faster turnaround (no need to fabricate)
  More visibility into design (“debugger” interface)
HDLs have features just for simulation
  Higher level data types: integers, FP-numbers, timestamps
  Routines for I/O: error messages, file operations
  Obviously, these cannot be synthesized into circuits
Also another reason for HDL/SDL confusion
  HDLs have “SDL” features for simulation
Notes: Verilog actually designed to support simulation more than synthesis – idea was you would come up with a design and then in the same language write code for testing the design hence a lot of constructs for doing looping and input output that are not related to hardware layout cannot be synthesized.

## Slide 35: FPGA “Design Flow”
Hardware compilers are generally much slower than their software counterparts
  solving hard problems: many more choices, optimizing for area, power, picosecond-level timing
HDL source code
netlist (wires, gates, FFs)
bitstream
implementation (place & route)
synthesis
simulation

## Slide 36: Side note: High-Level Synthesis
Translate “C to gates”
write hardware at a higher level of abstraction than conventional HDLs
  greater programmer productivity
  need to write stylized C that will synthesize well
  tools are still slow
  take ESE 532 to learn (much!) more