## Slide 1: 2. Instruction Set Architecture – Storage types and addressing modes

## Slide 2: Where do ISAs come into the game ?
MICROARCHITECTURE (Hardware implementation of the ISA) - Core i7 implements the x86 ISA - OMAP 4430 implements the ARM ISA
ARCHITECTURE – a.k.a. ISA (Instruction Set Architecture) - Platform-specific - a limited set of assembly language commands "understood“ by hardware (e.g. ADD, LOAD, STORE, RET)
Circuits
Devices
Compilers
Application software
The hw/sw
divide
Notes: X86 has around 1400 instructions, 300 basic types with variations
It is CISC (complex instruction set computer)
Not RISC (reduced instruction set computer)

## Slide 3: Basic von Neumann Architecture
Two Key Ideas
Data and instructions are in the same memory
  Programs (instructions) can be viewed as data and vice versa!
Instructions are stored sequentially in memory
  Accessed by the program counter (PC) —it contains the address/location of the instruction the hardware is executing
  The PC is simply incremented to “point to” the next instruction
  “jumps” / “branches” override fetching the sequential next insn
  Terminology: Jumps are usually unconditional and branches are conditional on a flag being checked
    there are conditional jumps….
How do we get the data?
  May be in registers or memory-–addressing modes

## Slide 4: Basic von Neumann Architecture
Here’s the (endless) loop that hardware repeats forever:
Fetch—get the next instruction–use the PC to find where it is in memory and place it in the instruction register
  The PC is changed to “point” to the next instruction in the program
  To make things simple, the von Neumann assumes the next instruction is placed sequentially in the memory
Decode—control logic examines the contents of the IR to decide what instruction it should perform
Execute—the outcome of the decoding process dictates
  an arithmetic or logical operation on data
  the kind of access to data in the same memory as the instructions
  OR the outcome is a change in the contents of the PC

## Slide 5: (Simplified) System Organization
Memory
Registers
+
X0 = 0
X1 = …
X2 = …
32 x 64 bits
CPU
Gigabytes to Terabytes
Load
Store
ALU
Address FFFF…
Address 0000

## Slide 6: Instruction Set Design – design space (1/2)
What instructions should be included?
  add, multiply, divide, sqrt [functions]
  branch [flow control]
  load/store [storage management]
What storage locations?
  How many registers?
  How much memory?
  Any other “architected” storage?
How should instructions be formatted?
  0, 1, 2 or more operands?
  Immediate operands
Notes: Mmx_add is a vector addition
Java bytecodes have mostly 0 operands - sometime 1

## Slide 7: Instruction Set Design – design space (2/2)
How to encode instructions?
  RISC (Reduced Instruction Set Computer): all instructions are same length (e.g. ARM, LC2K)
  CISC (Complex Instruction Set Computer): instructions can vary in size (Digital Equipment’s VAX, x86)
What instructions can access memory?
  For ARM and LC2K, only loads and stores can access memory (called a “load-store architecture”)
  Intel x86 is a “register-memory architecture”, that is, other instructions beyond ld/st can access memory
Notes: two characteristics of an ISA Load-store vs. memory and risc vs. cisc

## Slide 8: Why study Instruction Set Design?
Isn’t there only one?
  No, and even if there were, it would be too messy for a first course in computer architecture
How often are new architectures created?
  Embedded processors are designed all the time
  Even the Intel x86 ISA changes (MMX, MMX2, SSE, SSE2, AVX, … )
Will I ever get to (have to) design one?
  Very possible…
Notes: For that last bullet, it gets more likely via FPGAs and if and when hyper-specialized processors become common. Perhaps due to heterogeneous multicore.

## Slide 9: Software program to machine code
main()
{
int a, *b, c;
c = a + *b;
}
.text
.global main
r4 = load(r2);
r3 = add(r1,r4);
0x7456
0xA16B
C program
Assembly code
Machine code
Compile
Assemble
Example ISA
(simplified)
Notes: gcc –S to see your assembly code

## Slide 10: Assembly Code
Fields
  Opcode – What instruction to perform
  Source (input) operand specifier(s)
  Destination (output) operand specifier(s)
    What data to perform operation on
add
R2
100
R1
opcode
src1
src2
dest
value in r1 = contents of r2 + constant 100
Translation:
Example ISA
(simplified)
Notes: careful about sources and destinations
Different ISA have them in different positions
LC-2K last is dest
ARM first is dest

## Slide 11: Assembly Code characteristics
  Generally 1-1 correspondence with machine language
  Mnemonic codes facilitate programming
  Labels ( symbolic names )
  Direct control of the what processor does
  May execute fast, if you’re good at it, but compilers can typically generate better code
  Still hard to use and not portable to other brands of machines

## Slide 12: Assembly Code – ARM Example
25
X1
-4
X2
57
X3
ADD X3, X1, X2
ADDI X3, X3, #3
SUB X2, X3, X1
What are the contents of the registers after executing the given assembly code?
(1) ADD X3, X1, X2
25
X1
-4
X2
21
X3
(2) ADDI X3, X3, #3
25
X1
-4
X2
24
X3
(3) SUB X2, X3, X1
25
X1
-1
X2
24
X3
25
X1
-4
X2
57
X3
Program:
Initial
register file:
opcode d s1 s2imm
ARM v8 ISA
Notes: Comment on white space

## Slide 13: Assembly Instruction Encoding
Since the EDSAC (1949) almost all computers stored program instructions the same way they store data.
Each instruction is encoded as a number
add
R2
R3
R1
011011
010
011
001
011011010011001 = 20 + 23 + 24 + 27 + 29 + 210 + 212 + 213
= 13977
Example ISA
(simplified)

## Slide 14
Poll: How many different opcodes could be supported by this ISA? How many registers?
add
R2
R3
R1
011011
010
011
001
Example ISA
(simplified)

## Slide 15: Instruction Encoding (cont’d)
m bits can encode 2m different values
n values can be encoded in log2(n) bits
For above
  Can encode 26 = 64 opcodes
  Can encode 23 = 8 src/destination registers
How can we encode immediate operations, e.g., “add r2, r3, #4”?
add
R2
R3
R1
011011
010
011
001
Example ISA
(simplified)

## Slide 16: Instruction Encoding - Example
What is the max number of registers that can be designed in a machine given:
* 16-bit instructions
* Num. opcodes = 100
* All instructions are (reg, reg)  reg
(i.e., 2 source operands, 1 destination operand)
opcode
dest
src1
src2
16 bits
Example ISA
(simplified)
Poll: How many registers?

## Slide 17: Instruction Encoding - Example
What is the max number of registers that can be designed in a machine given:
* 16-bit instructions
* Num. opcodes = 100
* All instructions are (reg, reg)  reg
(i.e., 2 source operands, 1 destination operand)
opcode
dest
src1
src2
16 bits
num opcode bits = log2(100) = 7
num bits for operands = 16 –7 = 9
num bits per operand = 9 / 3 = 3
maximum number of registers = 2^3 = 8
Example ISA
(simplified)

## Slide 18: Class Problem
Given the following:
opcode
dest
src1
src2
3 bits
3 bits
3 bits
7 bits
What is the encoding for add R2, R3, R4 ? (R2 is dest, R3 is src1, and R4 is src2)
- add opcode is encoded as the number 53
- registers encoded with their register number
Example ISA
(simplified)
Poll: What is the encoding:
in binary
in hex
in decimal
Notes: 0110101010011100 / 6a9c / 27292

## Slide 19: Storage Architecture
Immediate Values
  Specifying constants in instructions
  Can't change during runtime… kinda like constants
Registers
  Fast and small (and useful)
Memory
  Big and complex (and useful)
Memory-mapped I/O
Notes: storage - show them the little intel video, show reg.file, caches, dimm (ram)
storage can be big and slow or small and fast

## Slide 20: 1. Immediate Values
= small constant values placed in instructions
They are stored in memory only because all instructions are in memory
Useful for loading small constants
  Example: ptr++;  addi R2, R2, #4
  Very useful for branch instructions
     target address is often immediate – in the instruction
Size of the immediate is usually determined by how many bits are left in the instruction format.
011111 010 010 100
Example ISA
(simplified)

## Slide 21: 2. Register Storage
First came the accumulator, a single register architecture
  Example: add #5
  You don’t need to specify which register when you only have one!
Register File
  Small array of memory-like storage
  Register access is faster than memory because register file arrays are small and can be put right next to the functional units in the processor.
Each register in the register file has a specific size
  e.g. 32-bit registers
Also called “register addressing”

## Slide 22: Example Architectures
ARMv8—LEGv8 subset from P+H text book
  32 registers (X0 – X31)
  64 bits in each register
  Some have special uses e.g. X31 is always 0—XZR
Intel x86
  4 general purpose registers (eax, ebx, ecx, edx) 32 bits
    You can treat them as two 8 or one 16-bits as well (ah, al, and ax)
  Special registers: 3 pointer registers (si,di,ip), 4 segment (cs,ds,ss,es),
  2 stack (sp, bp), status register (flags)
LC2K (the architecture you will be simulating)
  8 registers, 32 bits each
Notes: intel has to be backward compatible. it's a curse but also an advantage
(because it's hard to copy)

## Slide 23: Special Purpose Registers
Return address (ARM register X30 a.k.a. LR link register)
  Holds the return or link address of a subroutine
Stack pointer (x86 ESP register, ARM register X28 a.k.a SP)
  Holds the memory address of the “stack”
Frame pointer (ARM register X29 a.k.a. FP)
  Holds the memory address of the start of a stack frame
Status register (x86 EFLAGs register, ARM SPSR registers)
  Status bits set by various instructions
    Compare, add, etc.
  Status bits used by other instructions
    Conditional branches
0 value register (ARM register X31 a.k.a. XZR)
  No storage, reads always return 0 (lots of uses – ex: movadd)
  Implemented in SPARC and MIPS architectures
Program counter (usually referred to as PC)
  Cannot be accessed directly in most architectures
Notes: Global pointer: may be a dedicated register, or a gp register used as global pointer
By convention
Same for most others

## Slide 24: 3. Memory Storage
Large array of storage accessed using memory addresses
  A machine with a 32 bit address can reference memory locations 0 to 232-1 (or 4,294,967,295).
  A machine with a 64 bit address can reference memory locations 0 to 264-1
  (or 18,446,744,073,709,551,615—18 exa-locations)
Lots of different ways to calculate the address.
Notes: 4GBytes vs. 18 Exabytes
Lg 10 = 3.32

## Slide 25: Memory architecture: The ARM (Linux) Memory Image
Machine code instructions (and some constants)
Reserved for operating system
Global data and static local data
Dynamically allocated data—new or malloc()
Activation records: local variables, parameters, etc.
Stack
Heap data
Static data
Text
Reserved
0
Notes: Next time: take Ri out of here, it seems to be confusing, just focus on stack

## Slide 26: Addressing Modes
Direct addressing
Indirect addressing
Register indirect
Base + displacement
PC-relative
Strange addressing modes that made it into someone’s processor – and are interesting enough or ridiculous enough to talk about.

## Slide 27: Direct Addressing
Like register addressing
  Specify address as immediate constant
  load r1, M[1500] ; r1  contents of location 1500
  jump M[3000] ; jump to address 3000
Useful for addressing locations that don’t change during execution
  Branch target addresses
  Global/static variable locations
Example ISA
(simplified)
Notes: Show example of assembly format for these instructions

## Slide 28: Indirect Addressing
Compute the reference address by
  Specifying an immediate address
  Loading the value at that immediate address
  Using that value as the reference address
load r1, M[ M[1900] ]
2340
5555
0
1900
2340
Notes: inderect addressing used for **p

## Slide 29: Register indirect
Specify which register has the reference address
  Very useful for pointers
    load r1, M[ r2 ]
    add r2, r2, #4
    load r1, M[ r2 ]
3340
7777
6666
3340
3344
R2
register file
memory
6666
R1
Notes: register indirect used for *p

## Slide 30: Register indirect
Specify which register has the reference address
  Very useful for pointers
    load r1, M[ r2 ]
    add r2, r2, #4
    load r1, M[ r2 ]
7777
6666
3340
3344
register file
memory
3344
R2
6666
R1

## Slide 31: Register indirect
Specify which register has the reference address
  Very useful for pointers
    load r1, M[ r2 ]
    add r2, r2, #4
    load r1, M[ r2 ]
7777
6666
3340
3344
register file
memory
3344
R2
7777
R1

## Slide 32: Base + Displacement
Most common addressing mode today
Compute address as: reg value + immed
load r1, M [ r2 + 1000]
Good for accessing class objects/structures. Why?
a.tot += a.val;
2340
6666
5555
2340
3340
R2
register file
memory

## Slide 33: Class Problem
b. How can base + displacement be made to simulate indirect addressing?? (Hint: requires 2 instructions)
10
100
108
100
108
R2
104
-1
0
R1
108
R3
r2 = load M[r3]
r3 = load M[r2+4]
store M[r2+8], r3
a. What are the contents of register/memory after executing the following instructions
register file
memory
Example ISA
(simplified)
Notes: load Rx M[M[y] becomes
load Rt M[R0+ y]
load Rx M[Rt +0]

## Slide 34: PC-relative addressing
Variant on base + displacement
PC register is base, longer displacement possible since PC is assumed implicitly
  Used for branch instructions
    jump [ - 8 ] ; jump back 2 instructions (32-bit instructions)
Humans use labels and leave it to the assembler to determine the immediate value. Why?

## Slide 35: Other Addressing Modes
Double indirect
  load r1, M [ M [ M[1900]]]
Auto-increment
  load r1, M[ r2++ ]
  Implemented in earlier ARM ISA
  Often useful (why?)
Notes: autoincrement is useful to traverse vectors

## Slide 36: 4. Memory-mapped I/O
  Memory mapped I/O
  Sometimes I/O devices look like memory to the processor/OS (examples: graphic card, ethernet, etc.)
    So perhaps a keyboard where you read from a given address and you get the ASCII value of the last key pressed.