## Slide 1: CIS 501: Computer Architecture
Unit 5: Performance & Benchmarking
Slides developed by Joe Devietti, Milo Martin & Amir Roth at Upenn
with sources that included University of Wisconsin slides by Mark Hill, Guri Sohi, Jim Smith, and David Wood

## Slide 2: This Unit
Metrics
CPU Performance
Comparing Performance
Benchmarks
Performance Laws

## Slide 3: Performance Metrics

## Slide 4: Performance: Latency vs. Throughput
Latency (execution time): time to finish a fixed task
Throughput (bandwidth): number of tasks per unit time
  Different: exploit parallelism for throughput, not latency (e.g., bread)
  Often contradictory (latency vs. throughput)
    Will see many examples of this
  Choose definition of performance that matches your goals
    Scientific program? latency. web server? throughput.
Example: move people 10 miles
  Car: capacity = 5, speed = 60 miles/hour
  Bus: capacity = 60, speed = 20 miles/hour
  Latency: car = 10 min, bus = 30 min
  Throughput: car = 15 PPH (count return trip), bus = 60 PPH
Fastest way to send 10TB of data? (1+ gbits/second)
Notes: Answer: Used FedEx overnight to deliver the drive. 10 TB in, say, 15 hours is 1,300 mbits/second of bandwidth (600 GB/hour)

## Slide 5: CPU Performance

## Slide 6: Frequency as a performance metric
1 Hertz = 1 cycle per second 1 Ghz is 1 cycle per nanosecond, 1 Ghz = 1000 Mhz
(Micro-)architects often ignore dynamic instruction count…
… but general public (mostly) also ignores CPI
  and instead equate clock frequency with performance!
Which processor would you buy?
  Processor A: CPI = 2, clock = 5 GHz
  Processor B: CPI = 1, clock = 3 GHz
  Probably A, but B is faster (assuming same ISA/compiler)
Classic example
  Core i7 faster clock-per-clock than Core 2
  Same ISA and compiler!
partial performance metrics are dangerous!

## Slide 7: MIPS (performance metric, not the ISA)
(Micro) architects often ignore dynamic instruction count
  Typically work in one ISA/one compiler  treat it as fixed
CPU performance equation becomes
  Latency: seconds / insn = (cycles / insn) * (seconds / cycle)
  Throughput: insn / second = (insn / cycle) * (cycles / second)
MIPS (millions of instructions per second)
  Cycles / second: clock frequency (in MHz)
  Example: CPI = 2, clock = 500 MHz  0.5 * 500 MHz = 250 MIPS
Pitfall: may vary inversely with actual performance
  Compiler removes insns, program gets faster, MIPS goes down
  Work per instruction varies (e.g., multiply vs. add, FP vs. integer)
Notes: - Ie RISC vs CISC ins

## Slide 8: Cycles per Instruction (CPI)
CPI: Cycle/instruction on average
  IPC = 1/CPI
    Used more frequently than CPI
    Favored because “bigger is better”, but harder to compute with
  Different instructions have different cycle costs
    E.g., “add” typically takes 1 cycle, “divide” takes >10 cycles
  Depends on relative instruction frequencies
CPI example
  A program executes equal: integer, floating point (FP), memory ops
  Cycles per instruction type: integer = 1, memory = 2, FP = 3
  What is the CPI? (33% * 1) + (33% * 2) + (33% * 3) = 2
  Caveat: this sort of calculation ignores many effects
    Back-of-the-envelope arguments only
Notes: Q: what’s something that this CPI calc ignores?

## Slide 9: CPI Example
Assume a processor with instruction frequencies and costs
  Integer ALU: 50%, 1 cycle
  Load: 20%, 5 cycle
  Store: 10%, 1 cycle
  Branch: 20%, 2 cycle
Which change would improve performance more?
  A. “Branch prediction” to reduce branch cost to 1 cycle?
  B. Faster data memory to reduce load cost to 3 cycles?
Compute CPI
  Base = 0.5*1 + 0.2*5 + 0.1*1 + 0.2*2 = 2 CPI
Notes:   A = 0.5*1 + 0.2*5 + 0.1*1+ 0.2*1 = 1.8 CPI
  B = 0.5*1 + 0.2*3 + 0.1*1 + 0.2*2 = 1.6 CPI
A is 1.11x faster than base
B is 1.25x faster than base

## Slide 10: Measuring CPI
How are CPI and execution-time actually measured?
  Execution time? stopwatch timer (Unix “time” command)
  CPI = (CPU time * clock frequency) / dynamic insn count
  How is dynamic instruction count measured?
More useful is CPI breakdown (CPICPU, CPIMEM, etc.)
  So we know what performance problems are and what to fix
  Hardware event counters
    Available in most processors today
    One way to measure dynamic instruction count
    Calculate CPI using counter frequencies / known event costs
  Cycle-level micro-architecture simulation
    Measure exactly what you want … and impact of potential fixes!
    Method of choice for many micro-architects

## Slide 11: Comparing Performance

## Slide 12: Comparing Performance - Speedup
Speedup of A over B
  X = Latency(B)/Latency(A) (divide by the faster)
  X = Throughput(A)/Throughput(B) (divide by the slower)
A is X% faster than B if
  X = ((Latency(B)/Latency(A)) – 1) * 100
  X = ((Throughput(A)/Throughput(B)) – 1) * 100
  Latency(A) = Latency(B) / (1+(X/100))
  Throughput(A) = Throughput(B) * (1+(X/100))
Car/bus example
  Latency? Car is 3 times (and 200%) faster than bus
  Throughput? Bus is 4 times (and 300%) faster than car

## Slide 13: Speedup and % Increase and Decrease
Program A runs for 200 cycles
Program B runs for 350 cycles
Percent increase and decrease are not the same.
  % increase: ((350 – 200)/200) * 100 = 75%
  % decrease: ((350 - 200)/350) * 100 = 42.3%
Speedup:
  350/200 = 1.75 – Program A is 1.75x faster than program B
  As a percentage: (1.75 – 1) * 100 = 75%
If program C is 1x faster than A, how many cycles does C run for? – 200 (the same as A)
  What if C is 1.5x faster? 133 cycles (50% faster than A)

## Slide 14: Mean (Average) Performance Numbers
Arithmetic: (1/N) * ∑P=1..N P_latency
  For units that are proportional to time (e.g., latency)
Harmonic: N / ∑P=1..N 1/P_throughput
  For units that are inversely proportional to time (e.g., throughput)
You can add latencies, but not throughputs
  Latency(P1+P2,A) = Latency(P1,A) + Latency(P2,A)
  Throughput(P1+P2,A) != Throughput(P1,A) + Throughput(P2,A)
    1 mile @ 30 miles/hour + 1 mile @ 90 miles/hour
    Average is not 60 miles/hour
Geometric: N√∏P=1..N P_speedup
  For unitless quantities (e.g., speedup ratios)

## Slide 15: For Example…
You drive two miles
  30 miles per hour for the first mile
  90 miles per hour for the second mile
Question: what was your average speed?
  Hint: the answer is not 60 miles per hour
  Why?

## Slide 16: Answer
You drive two miles
  30 miles per hour for the first mile
  90 miles per hour for the second mile
Question: what was your average speed?
  Hint: the answer is not 60 miles per hour
  0.03333 hours per mile for 1 mile
  0.01111 hours per mile for 1 mile
  0.02222 hours per mile on average
  = 45 miles per hour
Notes: Q: avg if we drove 30mph for 1 hour and 60mph for 1 hour?

## Slide 17: Measurement Challenges

## Slide 18: Measurement Challenges
Are –O3 compiler optimizations really faster than –O0?
Why might they not be?
  other processes running
  not enough runs
  not using a high-resolution timer
  cold-start effects
  managed languages: JIT/GC/VM startup
solution: experiment design + statistics

## Slide 19: Experiment Design
Two kinds of errors: systematic and random
removing systematic error
  aka “measurement bias” or “not measuring what you think you are”
  Run on an unloaded system
  Measure something that runs for at least several seconds
  Understand the system being measured
    simple empty-for-loop test => compiler optimizes it away
  Vary experimental setup
  Use appropriate statistics
removing random error
  Perform many runs: how many is enough?
Notes: what problems does HW2 data collection have?

## Slide 20: Determining performance differences
Program runs in 20s on machine A, 20.1s on machine B
Is this a meaningful difference?
count
execution time
the distribution matters!
Notes: We can ask about average perf, 90% perf, etc.

## Slide 21: Confidence Intervals
Compute mean and confidence interval (CI)
Meaning of the 95% confidence interval x ± 1.3
  collected 1 sample with n experiments
  given repeated sampling, x will be within 1.3 of the true mean 95% of the time
If CIs overlap, differences not statistically significant
t = critical value from t-distribution
s = sample standard error
n = # experiments in sample
Notes: t depends on CI level

## Slide 22: CI example
setup
  130 experiments, mean = 45.4s, stderr = 10.1s
What’s the 95% CI?
t = 1.962 (depends on %CI and # experiments)
  look it up in a stats textbook or online
at 95% CI, performance is 45.4 ±1.74 seconds
What if we want a smaller CI?

## Slide 23: Benchmarking
Notes: metrics, stats, now need workloads

## Slide 24: Processor Performance and Workloads
Q: what does performance of a chip mean?
A: nothing, there must be some associated workload
  Workload: set of tasks someone (you) cares about
Benchmarks: standard workloads
  Used to compare performance across machines
  Either are, or highly representative of, actual programs people run
Micro-benchmarks: non-standard non-workloads
  Tiny programs used to isolate certain aspects of performance
  Not representative of complex behaviors of real applications
  Examples: binary tree search, towers-of-hanoi, 8-queens, etc.
Notes: -mention different workloads used for different purposes

## Slide 25: Example: SPECmark 2006/2017
performance wrt reference machine
Latency SPECmark
  For each benchmark
    Take odd number of samples
    Choose median
    Take speedup (reference machine / your machine)
  Take “average” (Geometric mean) of speedups over all benchmarks
Throughput SPECmark
  Run multiple benchmarks in parallel on multiple-processor system
Notes: Q: how does this account for run-to-run variability?

## Slide 26: Example: GeekBench
Set of cross-platform multicore benchmarks
  Can run on iPhone, Android, laptop, desktop, etc
Tests integer, floating point, memory bandwidth performance
GeekBench stores all results online
  Easy to check scores for many different systems, processors
Pitfall: Workloads are simple, may not be a completely accurate representation of performance
  We know they evaluate compared to a baseline benchmark
Notes:   geekbench workloads: GEMM, FFT, encryption, file/image (de)compress

## Slide 27: Example: GTA V
http://www.anandtech.com/show/9306/the-nvidia-geforce-gtx-980-ti-review
Notes: GTA V measures latency percentiles internally
sometimes, worst-case latency matters
google experiment: increase latency by 0.5s, 20% reduction in traffic/revenue
http://glinden.blogspot.com/2006/11/marissa-mayer-at-web-20.html

## Slide 28: Performance Laws

## Slide 29: Amdahl’s Law
How much will an optimization improve performance?
P = proportion of running time affected by optimization
S = speedup
What if I speedup 25% of a program’s execution by 2x?
1.14x speedup
What if I speedup 25% of a program’s execution by ∞?
1.33x speedup
Notes: 1-P is the runtime of unoptimized part
P/S is runtime of optimized part

## Slide 30: Amdahl’s Law for the US Budget
Chart: US Federal Gov’t Expenses 2017
| Total
Department of Education | 111702
Department of Agriculture | 127558
Department of Veterans Affairs | 176050
Department of the Treasury | 546397
all others | 558381
Department of Defense--Military Programs | 568896
Social Security Administration | 1000813
Department of Health and Human Services | 1116779
https://www.whitehouse.gov/omb/historical-tables/
scrapping Dept of Education ($111B) cuts budget by 2.7%
Notes: HHS includes Medicare/Medicaid
even Defense is ~13.5%

## Slide 31: Amdahl’s Law for Parallelization
How much will parallelization improve performance?
P = proportion of parallel code
N = threads
What is the max speedup for a program that’s 10% serial?
What about 1% serial?
Notes: 10% serial – 10x
1% serial – 100x

## Slide 32: Increasing proportion of parallel code
Amdahl’s Law requires extremely parallel code to take advantage of large multiprocessors
two approaches:
  strong scaling: shrink the serial component
    same problem runs faster
    becomes harder and harder to do
  weak scaling: increase the problem size
    natural in many problem domains: internet systems, scientific computing, video games
    doesn’t work in other domains

## Slide 33: Use Little’s Law!
How long am I going to be in this line?

## Slide 34: Little’s Law
Assumption:
  system is in steady state, i.e., average arrival rate = average departure rate
No assumptions about:
  arrival/departure/wait time distribution or service order (FIFO, LIFO, etc.)
Works on any queuing system
Works on systems of systems
L = λW
L = items in the system
λ = average arrival rate
W = average wait time

## Slide 35: Little’s Law for Computing Systems
Only need to measure two of L, λ and W
  often difficult to measure L directly
Describes how to meet performance requirements
  e.g., to get high throughput (λ), we need either:
    low latency per request (small W)
    service requests in parallel (large L)
Addresses many computer performance questions
  sizing queue of L1, L2, L3 misses
  sizing queue of outstanding network requests for 1 machine
    or the whole datacenter
  calculating average latency for a design

## Slide 36: Performance Rules of Thumb
Design for actual performance, not peak performance
  Peak performance: “Performance you are guaranteed not to exceed”
  Greater than “actual” or “average” or “sustained” performance
    Why? Caches misses, branch mispredictions, limited ILP, etc.
  For actual performance X, machine capability must be > X
Easier to “buy” bandwidth than latency
  say we want to transport more cargo via train:
    (1) build another track or (2) make a train that goes twice as fast?
  Use bandwidth to reduce latency
Build a balanced system
  Don’t over-optimize 1% to the detriment of other 99%
  System performance often determined by slowest component
Notes: System performance determined by “worst mistake” not by making everything perfect
- Build another track

## Slide 37: Measuring LC-4 Processor Performance
Notes: - Possibly move benchmarks before

## Slide 38: Benchmarking the LC-4 processors
Fixed workload: wireframe trace
Focus on improving frequency with pipelining
  measure frequency with Vivado timing reports
Focus on improving IPC with superscalar
  see how many cycles the wireframe trace takes
Notes: show results from Vivado timing report

## Slide 39: Summary
Latency = seconds / program =
  (instructions / program) * (cycles / instruction) * (seconds / cycle)
Instructions / program: dynamic instruction count
  Function of program, compiler, instruction set architecture (ISA)
Cycles / instruction: CPI
  Function of program, compiler, ISA, micro-architecture
Seconds / cycle: clock period
  Function of micro-architecture, technology parameters
Optimize each component
  this class focuses mostly on CPI (caches, parallelism)
  …but some on dynamic instruction count (compiler, ISA)
  …and some on clock frequency (pipelining, technology)