## Slide 1: 15. Basic Processor Design – Pipelining With Control Hazards

## Slide 2: Time graphs (a.k.a. pipe trace)
A vertical slice reports the entire activity of the pipeline at time 5
Time: 1 2 3 4 5 6 7 8 9
add
nor
lw
add
sw
fetch decode execute memory writeback
fetch decode execute memory writeback
fetch decode execute memory writeback
fetch decode execute memory writeback
fetch decode execute memory writeback

## Slide 3
3
PC
Inst
mem
REG
file
M
U
X
A
L
U
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
sign
ext
Control
Review: LC2k Pipelined Datapath

## Slide 4
4
What can go wrong?
Data hazards: since register reads occur in stage 2 and register writes occur in stage 5 it is possible to read the wrong value if is about to be written.
Control hazards: A branch instruction may change the PC, but not until stage 4. What do we fetch before that?
Exceptions: How do you handle exceptions in a pipelined processor with 5 instructions in flight?
  Exceptions are "programmed branches" to handle weird situations, like divide by zero
  Not covered in this class, take 373 / 470 to learn more

## Slide 5
5
Review: approaches to handling data hazards
Avoid
  Make sure there are no hazards in the code.
Detect and stall
  If hazards exist, stall the processor until they go away.
Detect and forward
  If hazards exist, fix up the pipeline to get the correct value (if possible).
Poll: In what situations do we stall (when forwarding)? (select all that apply)
Stores
Store followed by dependent
Loads
Loads followed by dependent
All instructions

## Slide 6
6
PC
Inst
mem
Register file
M
U
X
A
L
U
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
12
7
1
5
111
sw
noop
7
21
11
-2
14
99
0
8
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
data
M
U
X
H3
Data forwarding

## Slide 7
7
Example time graph
Time: | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
add 1 2 3 | IF | ID | EX | ME | WB |  |  |  |  |  |  |  | 
nor 3 4 5 |  | IF | ID | EX | ME | WB |  |  |  |  |  |  | 
add 6 3 7 |  |  | IF | ID | EX | ME | WB |  |  |  |  |  | 
lw 3 6 10 |  |  |  | IF | ID | EX | ME | WB |  |  |  |  | 
sw 6 2 12 |  |  |  |  | IF | ID* | ID | EX | ME | WB |  |  | 

## Slide 8
8
Pipeline function for BEQ
Fetch: read instruction from memory.
Decode: read source operands from registers.
Execute: calculate target address and test for equality.
Memory: Send target to PC if test is equal.
Writeback: Nothing left to do.
Branch outcomes
  Not Taken
    PC = PC + 1
  Taken
    PC = Branch Target Address

## Slide 9
9
Control hazards
beq 1 1 10
add 3 4 5
time
fetch decode execute memory writeback
fetch decode execute
beq
add

## Slide 10
10
Approaches to handling control hazards
Avoid
  Make sure there are no hazards in the code.
Detect and stall
  Delay fetch until branch resolved.
Speculate and Squash-if-Wrong
  Go ahead and fetch more instructions in case it is correct, but stop them if they shouldn’t have been executed.

## Slide 11
11
PC
Inst
mem
REG
file
M
U
X
A
L
U
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
sign
ext
Control
noop

## Slide 12
12
Control hazards
beq 1 1 10
add 3 4 5
time
fetch decode execute memory writeback
fetch fetch fetch
beq
add
fetch
or
fetch
Target:

## Slide 13
13
Problems with detect and stall
CPI increases every time a branch is detected!
Is that necessary? Not always!
  Branch not always taken.
  Let’s assume that it is NOT taken…
    In this case, we can ignore the beq (treat it like a noop).
    Keep fetching PC + 1.
  What if we are wrong?
    OK, as long as we do not COMPLETE any instructions we mistakenly executed.
    I.e., make changes that will be seen later such as changing register or memory values.

## Slide 14
14
Handling control hazards III: Speculate and squash
Speculate: assume not equal
  Keep fetching from PC+1 until we know that the branch is really taken.
Squash: stop bad instructions if taken
  Send a noop to Decode, Execute, and Memory.
  Send target address to PC.

## Slide 15
15
PC
REG
file
M
U
X
A
L
U
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
sign
ext
Control
equal
beq
sub
add
nor
add
sub
beq
beq
Inst
mem
noop
noop
noop

## Slide 16
16
Problems with fetching PC+1
CPI increases every time a branch is taken!
  About 50%-66% of time.
Is that necessary?
No! But how can you fetch from the target
before you even know the previous instruction
is a branch – much less whether it is taken?
Poll: If you had to guess, in real programs, what's the ratio of taken to not-taken branches?
Very rarely taken
Slightly biased towards not taken
Slightly biased towards taken
Very rarely not taken
Poll: If we take branches more often than not, why not have our design assume its taken?
Cuz we're dumb
Performance would actually be worse
We're missing information

## Slide 17
17
PC
Inst
mem
REG
file
M
U
X
A
L
U
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
sign
ext
Control
beq
bpc
target
target
eq?

## Slide 18: Branch Prediction
18
Predict the next fetch address (to be used in the next cycle)
Requires three things to be predicted at fetch stage:
  Whether the fetched instruction is a branch
  Branch direction (if conditional)
  Branch target address (if direction is taken)
Observation: Target address remains the same for a conditional direct branch across dynamic instances
  Store the target address from previous instance and access it with the PC
  Called Branch Target Buffer (BTB) or Branch Target Address Cache

## Slide 19: Fetch Stage with Branch Prediction
target address
Cache of Target Addresses (BTB: Branch Target Buffer)
Program
Counter
PC + inst size
taken?
Next Fetch
Address
hit?
Address of the
current branch
Direction predictor (2-bit counters)
19

## Slide 20: Branch Direction Prediction
"Branch direction" refers to whether the branch was taken or not
Two methods for predicting direction:
  Static - We predict once during compilation, and that prediction never changes
  Dynamic - We predict (potentially) many times during execution, and the prediction may change over time
Static vs dynamic strategies are a very common topic in computer architecture

## Slide 21: Branch Direction Prediction
Compile time (static)
  Always not taken
  Always taken
  BTFN (Backward taken, forward not taken)
  Profile based (likely direction)
  Program analysis based (likely direction)
Run time (dynamic)
  Last time prediction (single-bit)
  Two-bit counter based prediction
  Two-level prediction (global vs. local)
  Hybrid
21

## Slide 22: Branch Direction Prediction (Static)
Always not-taken
  Simple to implement: no need for BTB, no direction prediction
  Low accuracy: ~30-40%
  Compiler can layout code such that the likely path is the “not-taken” path
Always taken
  No direction prediction
  Better accuracy: ~60-70%
    Backward branches (i.e. loop branches) are usually taken
    Backward branch: target address lower than branch PC
Backward taken, forward not taken (BTFN)
  Predict backward (loop) branches as taken, others not-taken
22

## Slide 23: Branch Direction Prediction (Dynamic)
Last time predictor
  Single bit per branch (stored in BTB)
  Indicates which direction branch went last time it executed
  TTTTTTTTTTNNNNNNNNNN  90% accuracy
Always mispredicts the last iteration and the first iteration of a loop branch
  Accuracy for a loop with N iterations = (N-2)/N
+ Loop branches for loops with large number of iterations
-- Loop branches for loops will small number of iterations
TNTNTNTNTNTNTNTNTNTN  0% accuracy
23

## Slide 24: State Machine for Last-Time Prediction
predict
taken
predict
not
taken
actually
not taken
actually
taken
actually
taken
actually
not taken
24

## Slide 25: Improving the Last Time Predictor
Problem: A last-time predictor changes its prediction from TNT or NTT too quickly
  Even though the branch may be mostly taken or mostly not taken
Solution Idea: Add hysteresis to the predictor so that prediction does not change on a single different outcome
  Use two bits to track the history of predictions for a branch instead of a single bit
  Can have 2 states for T or NT instead of 1 state for each
25

## Slide 26: Two-Bit Counter Based Prediction
Each branch associated with a two-bit counter
One more bit provides hysteresis
A strong prediction does not change with one single different outcome
  + Better prediction accuracy
  -- More hardware cost (but counter can be part of a BTB entry)
26

## Slide 27: State Machine for 2-bit Saturating Counter
pred
taken
11
pred
taken
10
pred
!taken
01
pred
!taken
00
actually
taken
actually
taken
actually
!taken
actually
!taken
actually
!taken
actually
!taken
actually
taken
actually
taken
“weakly
taken”
“strongly
taken”
“weakly
!taken”
“strongly
!taken”
27

## Slide 28: Two-Bit Counter Based Prediction
What’s the prediction accuracy of a branch with the following sequence of taken/not taken evaluations
    T T T T N T T N N N T N T N N
Br
State
Pred
T
11
T
T
11
T
T
11
T
N
11
T
T
10
T
T
11
T
N
11
T
N
10
T
N
01
N
T
00
N
N
01
N
T
00
N
N
01
N
N
00
N
10
T
T
28

## Slide 29
Branch prediction
Predict not taken: ~50% accurate.
Predict backward taken: ~65% accurate.
Predict same as last time: ~80% accurate.
Pentium: ~85% accurate.
Pentium Pro: ~92% accurate.
Best paper designs: ~96% accurate.
29