## Slide 1: 16. Basic Processor Design – Exceptions and Pipeline Performance

## Slide 2: Building with Pipelines
CPI for pipelining:
  1 (ideal case - no stalls)
  > 1 (reality, depends on program)
What if we want to improve performance more?
  Want CPI as low as possible – lower than 1
Use Parallelism
  Instruction Level Parallelism (ILP) – Within task
  Thread Level Parallelism (TLP) – Having many tasks
  Data Level Parallelism (DLP) – Many tasks with same instructions

## Slide 3
3
Calculating performance with no stalls
add 1 2 3
nor 1 4 5
add 4 6 7
How many cycles does this
code take to execute?
What value is written to the
ALU result field of the Mem/WB
pipeline register at the end of cycle 5.
Notes: No stalls. Final WB is in cycle 7 cycles (5+2). NAND result goes to Mem/WB in cycle 5.

## Slide 4
4
Calculating performance with no stalls
add 1 2 3
nor 1 4 5
add 4 6 7
How many cycles does this
code take to execute?
What value is written to the
ALU result field of the Mem/WB
pipeline register at the end of cycle 5.
No stalls – Final WB @ cycle 7
nor result
Notes: No stalls. Final WB is in cycle 7 cycles (5+2). NAND result goes to Mem/WB in cycle 5.

## Slide 5
5
Calculating performance with data hazards (detect and stall)
add 1 2 3
nor 3 4 5
add 3 5 6
How many data hazards are there
in this code?
How many stall cycles if we use
detect and stall to handle the
hazards?
Time: | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
add 1 2 3 | IF | ID | EX | ME | WB |  |  |  |  |  | 
nand 3 4 5 |  |  |  |  |  |  |  |  |  |  | 
add 3 5 6 |  |  |  |  |  |  |  |  |  |  | 
Notes: Add to nand via 3, add to add via 3, nand to add via 5.
Detect and stall adds 2 cycles ea for nand and final add. 11 cycles

## Slide 6
6
Calculating performance with data hazards (detect and stall)
add 1 2 3
nor 3 4 5
add 3 5 6
How many data hazards are there
in this code?
How many stall cycles if we use
detect and stall to handle the
hazards?
3 data hazards
Stall : 4 cycles
Total : 11 cycles
Time: | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
add 1 2 3 | IF | ID | EX | ME | WB |  |  |  |  |  | 
nor 3 4 5 |  | IF | ID* | ID* | ID | EX | ME | WB |  |  | 
add 3 5 6 |  |  | IF* | IF* | IF | ID* | ID* | ID | EX | ME | WB
Notes: Add to nand via 3, add to add via 3, nand to add via 5.
Detect and stall adds 2 cycles ea for nand and final add. 11 cycles

## Slide 7
7
Calculating performance with data hazards (detect and forward)
add 1 2 3
nor 3 4 5
add 3 5 6
lw 3 6 7
add 6 6 1
Where do the values for the second add
instruction come from?
How many stall cycles on the
LC2K pipelined datapath with
data forwarding from lecture?
Notes: Bypass from ex
w/ forwarding, we have 1 stall cycle (lw->add)

## Slide 8
8
Calculating performance with data hazards (detect and forward)
add 1 2 3
nor 3 4 5
add 3 5 6
lw 3 6 7
add 6 6 1
Where do the values for the second add
instruction come from?
How many stall cycles on the
LC2K pipelined datapath with
data forwarding from lecture?
From Mem/WB and EX/Mem
1 stall for lw ➜ add
Notes: Bypass from ex
w/ forwarding, we have 1 stall cycle (lw->add)

## Slide 9
9
Calculating performance with control hazards (speculate and squash)
How many cycles are saved if you perform speculate and squash for the following code (assume that branches are predicted to be not taken)?
Assume the branch is taken: How many cycles to execute this code?
Assume the branch is not taken: How many cycles execute this code?
add 1 2 3
beq 1 5 1
nor 6 4 1
add 3 4 5
Notes: Saves 3 clocks

## Slide 10
10
Calculating performance with control hazards (speculate and squash)
How many cycles are saved if you perform speculate and squash for the following code (assume that branches are predicted to be not taken)?
Assume the branch is taken: How many cycles to execute this code?
Assume the branch is not taken: How many cycles execute this code?
add 1 2 3
beq 1 5 1
nor 6 4 1
add 3 4 5
3 instr + 3 stalls + 4 to empty pipe = 10 cycles
4 instr + 4 to empty pipe = 8 cycles
Notes: Saves 3 clocks

## Slide 11
11
Calculating performance with control hazards
add 1 2 3
beq 1 5 1
lw 6 4 1
add 3 4 5
beq 5 7 -5
halt
Assume the first branch is taken 50% of the time and the loop iterates 100 times, and forwarding for all data hazards.
  How many cycles does the code take assuming detect and stall for control hazards?
Assume halt is resolved in WB stage

## Slide 12
12
Calculating performance with control hazards
Assume the first branch is taken 50% of the time and the loop iterates 100 times, and forwarding for all data hazards.
  How many cycles does the code take assuming detect and stall for control hazards?
# Instructions = 100*(0.5*5 + 0.5*4) + 1 = 451
Time = 451 + load stalls + branch stalls + empty pipe
Time = 451 + 100*0.5*1 +
Time = 451 + 100*0.5*1 + (100*3 + 100*3) + 4
Time = 1105
add 1 2 3
beq 1 5 1
lw 6 4 1
add 3 4 5
beq 5 7 -5
halt

## Slide 13
13
Calculating performance with control hazards
Assume the first branch is taken 50% of the time and the loop iterates 100 times, and forwarding for all data hazards.
  How many cycles does the code take assuming speculate and squash where all branches are predicted not taken?
add 1 2 3
beq 1 5 1
lw 6 4 1
add 3 4 5
beq 5 7 -5
halt

## Slide 14
14
Calculating performance with control hazards
Assume the first branch is taken 50% of the time and the loop iterates 100 times, and forwarding for all data hazards.
  How many cycles does the code take assuming speculate and squash where all branches are predicted not taken?
# Instructions = 100*(0.5*5 + 0.5*4) + 1 = 451
Time = 451 + load stalls + branch stalls + empty pipe
Time = 451 + 100*0.5*1 + (100*0.5*3 + 99*3) + 4
Time = 952
add 1 2 3
beq 1 5 1
lw 6 4 1
add 3 4 5
beq 5 7 -5
halt

## Slide 15
15
Calculating performance with control hazards
Assume the first branch is taken 50% of the time and the loop iterates 100 times, and forwarding for all data hazards.
  How many cycles does the code take assuming speculate and squash where backward branches are predicted taken and forward branches not taken?
add 1 2 3
beq 1 5 1
lw 6 4 1
add 3 4 5
beq 5 7 -5
halt

## Slide 16
16
Calculating performance with control hazards
Assume the first branch is taken 50% of the time and the loop iterates 100 times, and forwarding for all data hazards.
  How many cycles does the code take assuming speculate and squash where backward branches are predicted taken and forward branches not taken, andBTB has all entrys to start?
# Instructions = 100*(0.5*5 + 0.5*4) + 1 = 451
Time = 451 + load stalls + branch stalls + empty pipe
Time = 451 + 100*0.5*1 + (100*0.5*3 + 1*3) + 4
Time = 658
add 1 2 3
beq 1 5 1
lw 6 4 1
add 3 4 5
beq 5 7 -5
halt

## Slide 17
17
Calculating performance with control hazards
Assume the first branch has the pattern TTTN that repeats, and the loop is iterated 100 times
  How many cycles does the code take if a 2-bit counter BTB is used to predict each branch, how many cycles does the code take? Assume initial state of branch predictor counter is “10” (WT)
add 1 2 3
beq 1 5 1
lw 6 4 1
add 3 4 5
beq 5 7 -5
halt

## Slide 18
18
Calculating performance with control hazards
Assume the first branch has the pattern TTTN that repeats, and the loop is iterated 100 times
  How many cycles does the code take if a 2-bit counter BTB is used to predict each branch, how many cycles does the code take? Assume initial state of branch predictor counter is “10” (WT)
T T T N
X
√
√
√
T T T N
X
√
√
√
T T T N
X
√
√
√
•
•
•
beq 1
# Instructions = 100*(0.25*5 + 0.75*4) + 1 = 426
Time = 426 + load stalls + branch stalls + empty pipe
Time = 426 + 100*0.25*1 + 100*0.25*3 + 1*3 + 4
Time = 533
beq 2 is correct 99 times, then incorrect last iter
add 1 2 3
beq 1 5 1
lw 6 4 1
add 3 4 5
beq 5 7 -5
halt

## Slide 19
19
Classic performance problem
Program with following instruction breakdown:
lw 10%
sw 15%
beq 25%
R-type 50%
Speculate “always not-taken” and squash. 80% of branches not-taken
Full forwarding to execute stage. 20% of loads stall for 1 cycle
What is the CPI of the program?
What is the total execution time if cycle time is 100MHz?
Notes: CPI = 1 + 0.10*0.20*1 + 0.25*0.20*3
CPI = 1 + 0.02 + 0.15
CPI = 1.17

## Slide 20
20
Classic performance problem
Program with following instruction breakdown:
lw 10%
sw 15%
beq 25%
R-type 50%
Speculate “always not-taken” and squash. 80% of branches not-taken
Full forwarding to execute stage. 20% of loads stall for 1 cycle
What is the CPI of the program?
What is the total execution time if cycle time is 100MHz?
CPI = 1 + 0.10 (loads) * 0.20 (load use stall)*1
+ 0.25 (branch) * 0.20 (miss rate)*3
CPI = 1 + 0.02 + 0.15 = 1.17
Time = 1.17 * 10ns = 11.7ns
Notes: CPI = 1 + 0.10*0.20*1 + 0.25*0.20*3
CPI = 1 + 0.02 + 0.15
CPI = 1.17

## Slide 21
21
Classic performance problem (cont.)
Assume branches are resolved at Execute?
  What is the CPI?
  What happens to cycle time?
  What is the total execution time?

## Slide 22
22
Classic performance problem (cont.)
Assume branches are resolved at Execute?
  What is the CPI?
  What happens to cycle time?
  What is the total execution time?
CPI = 1 + 0.10 (loads) *0.20 (load use stall)*1
+ 0.25 (branch) * 0.20 (miss rate)*2
CPI = 1 + 0.02 + 0.1 = 1.12