## Slide 1: CIS 501 Computer Organization and Design
Unit 9: Superscalar Pipelines
Slides developed by M. Martin, A. Roth, C.J. Taylor and Benedict Brown at the University of Pennsylvania with sources that included University of Wisconsin slides by Mark Hill, Guri Sohi, Jim Smith, and David Wood.

## Slide 2: A Key Theme: Parallelism
Previously: pipeline-level parallelism
  Work on execute of one instruction in parallel with decode of next
Next: instruction-level parallelism (ILP)
  Execute multiple independent instructions fully in parallel
Then:
  Static & dynamic scheduling
    Extract much more ILP
  Data-level parallelism (DLP)
    Single-instruction, multiple data (one insn., four 64-bit adds)
  Thread-level parallelism (TLP)
    Multiple software threads running on multiple cores

## Slide 3: An Opportunity…
But consider:
  ADD r1, r2 -> r3
  ADD r4, r5 -> r6
  Why not execute them at the same time? (We can!)
What about:
  ADD r1, r2 -> r3
  ADD r4, r3 -> r6
  In this case, dependences prevent parallel execution
What about three instructions at a time?
  Or four instructions at a time?

## Slide 4: What Checking Is Required?
For two instructions: 2 checks
  ADD src11, src21 -> dest1
  ADD src12, src22 -> dest2 (2 checks)
For three instructions: 6 checks
  ADD src11, src21 -> dest1
  ADD src12, src22 -> dest2 (2 checks)
  ADD src13, src23 -> dest3 (4 checks)
For four instructions: 12 checks
  ADD src11, src21 -> dest1
  ADD src12, src22 -> dest2 (2 checks)
  ADD src13, src23 -> dest3 (4 checks)
  ADD src14, src24 -> dest4 (6 checks)
Plus checking for load-to-use stalls from prior n loads

## Slide 5: What Checking Is Required?
For two instructions: 2 checks
  ADD src11, src21 -> dest1
  ADD src12, src22 -> dest2 (2 checks)
For three instructions: 6 checks
  ADD src11, src21 -> dest1
  ADD src12, src22 -> dest2 (2 checks)
  ADD src13, src23 -> dest3 (4 checks)
For four instructions: 12 checks
  ADD src11, src21 -> dest1
  ADD src12, src22 -> dest2 (2 checks)
  ADD src13, src23 -> dest3 (4 checks)
  ADD src14, src24 -> dest4 (6 checks)
Plus checking for load-to-use stalls from prior n loads

## Slide 6: How do we build such “superscalar” hardware?

## Slide 7: Superscalar Pipeline Diagrams - Ideal
scalar | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
lw 0(r1)r2 | F | D | X | M | W |  |  |  |  |  |  | 
lw 4(r1)r3 |  | F | D | X | M | W |  |  |  |  |  | 
lw 8(r1)r4 |  |  | F | D | X | M | W |  |  |  |  | 
add r14,r15r6 |  |  |  | F | D | X | M | W |  |  |  | 
add r12,r13r7 |  |  |  |  | F | D | X | M | W |  |  | 
add r17,r16r8 |  |  |  |  |  | F | D | X | M | W |  | 
lw 0(r18)r9 |  |  |  |  |  |  | F | D | X | M | W | 
2-way superscalar | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
lw 0(r1)r2 | F | D | X | M | W |  |  |  |  |  |  | 
lw 4(r1)r3 | F | D | X | M | W |  |  |  |  |  |  | 
lw 8(r1)r4 |  | F | D | X | M | W |  |  |  |  |  | 
add r14,r15r6 |  | F | D | X | M | W |  |  |  |  |  | 
add r12,r13r7 |  |  | F | D | X | M | W |  |  |  |  | 
add r17,r16r8 |  |  | F | D | X | M | W |  |  |  |  | 
lw 0(r18)r9 |  |  |  | F | D | X | M | W |  |  |  | 
Notes: Like Noah’s ark the instructions come in 2 by two.

## Slide 8: Superscalar Pipeline Diagrams - Realistic
scalar | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
lw 0(r1)r2 | F | D | X | M | W |  |  |  |  |  |  | 
lw 4(r1)r3 |  | F | D | X | M | W |  |  |  |  |  | 
lw 8(r1)r4 |  |  | F | D | X | M | W |  |  |  |  | 
add r4,r5r6 |  |  |  | F | D | d* | X | M | W |  |  | 
add r2,r3r7 |  |  |  |  |  | F | D | X | M | W |  | 
add r7,r6r8 |  |  |  |  |  |  | F | D | X | M | W | 
lw 4(r8)r9 |  |  |  |  |  |  |  | F | D | X | M | W
2-way superscalar | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
lw 0(r1)r2 | F | D | X | M | W |  |  |  |  |  |  | 
lw 4(r1)r3 | F | D | X | M | W |  |  |  |  |  |  | 
lw 8(r1)r4 |  | F | D | X | M | W |  |  |  |  |  | 
add r4,r5r6 |  | F | D | d* | d* | X | M | W |  |  |  | 
add r2,r3r7 |  |  | F | D | d* | X | M | W |  |  |  | 
add r7,r6r8 |  |  |  |  | F | D | X | M | W |  |  | 
lw 4(r8)r9 |  |  |  |  | F | d* | D | X | M | W |  | 

## Slide 9: Superscalar Implementation Challenges

## Slide 10: Superscalar Challenges - Front End
Superscalar instruction fetch
  Modest: fetch multiple instructions per cycle
  Aggressive: buffer instructions and/or predict multiple branches
Superscalar instruction decode
  Replicate decoders
Superscalar instruction issue
  Determine when instructions can proceed in parallel
  More complex stall logic - order N2 for N-wide machine
  Not all combinations of types of instructions possible
Superscalar register read
  Port for each register read (4-wide superscalar  8 read “ports”)
  Each port needs its own set of address and data wires
    Latency & area  #ports2

## Slide 11: Superscalar Challenges - Back End
Superscalar instruction execution
  Replicate arithmetic units (but not all, for example, integer divider)
  Perhaps multiple cache ports (slower access, higher energy)
    Only for 4-wide or larger (why? only ~35% are load/store insn)
Superscalar bypass paths
  More possible sources for data values
  Order (N2 * P) for N-wide machine with execute pipeline depth P
Superscalar instruction register writeback
  One write port per instruction that writes a register
  Example, 4-wide superscalar  4 write ports
Fundamental challenge:
  Amount of ILP (instruction-level parallelism) in the program
  Compiler must schedule code and extract parallelism