## Slide 1: 17. Cache organization: The basics

## Slide 2: Today’s Lecture: Cache Organization Basics
Cache
Caches consume most of a processor’s die area

## Slide 3: Cache Aware vs Non-Aware Code
Notes: Time: 2.7 seconds vs 16.4 seconds

## Slide 4
Memory
So far, we have discussed two structures that hold data:
  Register file (little array of words)
  Memory (bigger array of words)
We have discussed several methods of implementing storage devices:
  Static memory (made with logic gates)
  Dynamic memory (transistor and capacitor)
  ROM, and other ROM-like storage, e.g., flash (floating gate transistors)
4

## Slide 5
Memory Hierarchy
We want a lot of memory
  LC2 can handle 218 bytes of memory
  MIPS can handle 232 bytes of memory
  Athlon-64 or EM64T can handle 264 bytes of memory
What are our choices?
  SRAM, DRAM, ROM, Flash, disk, tape, optical disk?

## Slide 6
Option 1: SRAM
Fast: ~2ns access time or faster
  Decoders are big
  Array is big
    Why?
Expensive, high area requirement
  SRAM: ~$5.0 per megabyte
    $0.13 for LC2
    $20,000 for MIPS
    $88,000,000,000,000 for Athlon-64

## Slide 7
Option 2: DRAM
Slower: ~60ns access time
  Must stall for dozens of cycles on each memory load
Less expensive than SRAM.
  DRAM costs ~$0.004 per megabyte
      $0.00 for LC2
      $16for MIPS/Pentium-IV/Athlon-XP
      $70,000,000,000 for Alpha/G5/x86_64

## Slide 8
Option 3: Disks
Obnoxiously slow: 3,000,000ns access time
  We could have stopped with the Intel 4004
Cheap
  Disk storage costs $0.000043 per megabyte
      $0.00 LC2
      $0.18 for MIPS
      $760,000,000 for Athlon-64
Non-volatile

## Slide 9
Memory Hierarchy Goals
Fast: Ideally run at processor clock speed
  1 ns access
Cheap: Ideally free
  Not more expensive than rest of system
Options DRAM, flash, disks are too slow
Option SRAM is too expensive
How to get best properties of multiple memory technologies?

## Slide 10: Memory Hierarchy Goals
fast
small
big but slow
move what you use here
backup
everything
here
With good locality of reference, memory appears as fast as
and as large as
faster per byte
cheaper per byte

## Slide 11
Memory Hierarchy
Use a small array of SRAM
  Small so fast and cheap
  For the cache (hopefully covers most loads and stores)
Use a larger amount of DRAM
  Cheaper than SRAM, faster than flash/disk
  For the main memory
Use a lot of flash and/or disk
  Non-volatile. Cheap. Big
  For Virtual memory
Don’t try to buy 264 bytes of anything
  Use “virtual memory” to make it look like the entire address range is available
  A few TB is enough for most desktop machines today, or a smartphone in a few years

## Slide 12
12
Memory hierarchy
Cache
(SRAM)
Main memory
(DRAM)
Disk
(magnetic or floating gate)
Cost
Latency

## Slide 13
Function of the Cache
The cache will hold the data that we think is most likely to be referenced
  Because we want to maximize the number of references that are serviced by the cache to minimize the average memory access latency
  How do we decide what the most likely accessed memory locations are?

## Slide 14: Hardware Background
Content Addressable Memory（内容寻址存储器）
Unlike regular memory, where we insert an index (or address) and it gives us data…
For a CAM, we insert data and get an index (or a bit saying it's not in there)

## Slide 15
CAM example
101101101
101101000
100101111
111101101
110001101
111101101
Found location 3
5 storage element CAM array of 9 bits each

## Slide 16
Operations on CAMs
Search: the primary way to access a CAM
  Send data to CAM memory
  Return “found” or “not found”
  If found, return location of where it was found or associated value
Write:
  Send data for CAM to remember
    Where should it be stored if CAM is full?
      Replacement policy
        Replace oldest data in the CAM
        Replace least recently searched data

## Slide 17
Previous use of CAMs
You have seen a simple CAM used before. When?

## Slide 18: Fetch Stage with Branch Prediction
target address
Cache of Target Addresses (BTB: Branch Target Buffer)
Program
Counter
PC + inst size
taken?
Next Fetch
Address
hit?
Address of the
current branch
Direction predictor (2-bit counters)

## Slide 19
Basic Cache Design
Cache memory can copy data from any part of main memory. It has 2 parts:
  The TAG (CAM) holds the memory address
  The BLOCK (SRAM) holds the memory data
Accessing the cache: compare reference address and tag
  Match? Get the data from the cache block
  No Match? Get the data from main memory
TAG BLOCK
data
addr
data
addr

## Slide 20: Cache Organization
A cache memory consists of multiple tag/block pairs (called cache lines)
  Searches can be done in parallel (within reason)
  At most one tag will match
If there is a tag match, it is a cache HIT
If there is no tag match, it is a cache MISS
  Our goal is to keep the data we think will be accessed in the near future in the cache
TAG BLOCK
data
addr
data
addr

## Slide 21: Caches: the hardware view
A hit in the cache
A miss in the cache
CAM SRAM
0x8060c000
0x0040a0c0
0x0345b480
0x04563900
150
0
-355
450
0x0040a0c0
search result
01
TAG BLOCK
0
From the µp
To the µp
0x8060c000
0x0040a0c0
0x0345b480
0x04563900
150
0
-355
450
0x0050a0c0
search result
Not found
TAG BLOCK
CAM SRAM
From the µp
To the main memory
0x0050a0c0

## Slide 22: Cache Operation
Every cache miss will get the data from memory and ALLOCATE a cache line to put the data in
  Just like any CAM write
Which line should be allocated?
  Random? OK, but hard to grade test questions
  Better than random? How?

## Slide 23: Something To Think About
Does an optimal replacement policy exist?
  That is, given a choice of cache lines to replace, which one will result in the fewest total misses during program execution
  Hint: a crystal ball will come in handy in solving this problem…
Why would we care?

## Slide 24: Picking the Most Likely Addresses
What is the probability of accessing a random memory location?
  With no information, it is just as likely as any other address
But programs are not random
  They tend to use the same memory locations over and over
  We can use this to pick the most referenced locations to put into the cache

## Slide 25: Temporal Locality
The principle of temporal locality in program references says that if you access a memory location (e.g., 1000) you will be more likely to re-access that location than you will be to reference some other random location
Temporal locality says any miss data should be placed into the cache
  It is the most recent reference location
Temporal locality says that the least recently referenced (or least recently used – LRU ) cache line should be evicted to make room for the new line
  Because the re-access probability falls over time as a cache line isn’t referenced, the LRU line is least likely to be re-referenced

## Slide 26: A Very Simple Memory System
74
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
tag data
R0
R1
R2
R3
Memory
2 cache lines
4 bit tag field
1 byte block
V
V

## Slide 27: A Very Simple Memory System
74
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
tag data
R0
R1
R2
R3
Memory
Is it in the cache?
No valid tags
This is a
Cache miss
Allocate: address  tag
Mem[1]  block
1
110
0
0
1

## Slide 28: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
tag data
R0
R1
R2
R3
Memory
110
lru
Misses: 1
Hits: 0
110
74
1
0

## Slide 29: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
tag data
R0
R1
R2
R3
Memory
110
Misses: 1
Hits: 0
110
lru
74
Check tags: 5  1
Cache Miss
1
0
1
150
5

## Slide 30: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
5
tag data
R0
R1
R2
R3
Memory
110
150
Misses: 2
Hits: 0
110
lru
74
150
1
1

## Slide 31: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
5
tag data
R0
R1
R2
R3
Memory
110
150
Misses: 2
Hits: 0
110
150
lru
74
Check tags: 1  5,
but 1 = 1 (HIT!)
1
1

## Slide 32: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
5
tag data
R0
R1
R2
R3
Memory
110
150
Misses: 2
Hits: 1
110
150
lru
74
110
1
1

## Slide 33: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
5
tag data
R0
R1
R2
R3
Memory
110
150
Misses: 2
Hits: 1
110
150
lru
74
110
1
1

## Slide 34: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
5
tag data
R0
R1
R2
R3
Memory
110
150
Misses: 2
Hits: 1
110
150
lru
74
110
7  5 and 7  1
(MISS!)
170
170
1
1
7

## Slide 35: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
7
tag data
R0
R1
R2
R3
Memory
110
170
Misses: 3
Hits: 1
110
150
170
lru
74
1
1

## Slide 36: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
7
tag data
R0
R1
R2
R3
Memory
110
170
Misses: 3
Hits: 1
110
150
170
lru
74
7  1 and 7 = 7
(HIT!)
170
1
1

## Slide 37: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
7
tag data
R0
R1
R2
R3
Memory
110
170
Misses: 3
Hits: 2
110
170
170
lru
74
1
1

## Slide 38: Calculating Average Access Latency
Avg latency = cache latency  hit rate + memory latency  miss rate
Avg latency for our example cache = 1 cycle  (2/5) + 15  (3/5) = 9.4 cycles per reference
To improve average latency:
  Improve memory access latency, or
  Improve cache access latency, or
  Improve cache hit rate

## Slide 39: Calculating Cost
How much does our example cache cost (in bits)?
  Calculate storage requirements
    2 bytes of SRAM
  Calculate overhead to support access (tags)
    2 4-bit tags
    The cost of the tags is often forgotten for caches, but this cost drives the design of real caches
    2 valid bits
What is the cost if a 32 bit address is used?

## Slide 40: How can we reduce the overhead?
Have a small address.
  Impractical, and caches are supposed to be micro-architectural
Cache bigger units than bytes
  Each block has a single tag, and blocks can be whatever size we choose.
To Be Continued…