## Slide 1: 21. Cache Organization: Wrapup & Practice Problems

## Slide 2
This slide just here to remind Jon to record

## Slide 3: ANNOUNCEMENTS
Discussion pods today
HW 5 is due next Tuesday
Project 4 release later today

## Slide 4: Poll
Poll: A direct-mapped cache can be though of as a set-associative cache with 1 ______?
block
tag
set
way

## Slide 5: Review: Set-associative cache
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
tag data
78
120
71
173
21
28
200
225
tag
set index
block offset
Address:
Set 0
Set 1
1 bit
1 bits
2 bit
Way0
Way1
Memory
Each memory location maps to a specific "set" (color)
Within a "set", a piece of data can be stored in any "way"
Poll: How many tag bits are required? What are the overheads?

## Slide 6: Review: The 3C’s of Cache Misses
First reference to an address
  Compulsory miss
    Also sometimes called a “cold start” miss
    First reference to any block will always miss
Cache is too small to hold all the data
  Capacity miss
    Would have had a hit with a large enough cache
Replaced it from a busy set
  Conflict miss
    Would have had a hit with a fully associative cache

## Slide 7: Review: Classifying Cache Misses
Can you classify all cache misses?
  Compulsory miss?
  Capacity miss?
  Conflict miss?
Yes! (with a cache simulator)
  Simulate with a cache of unlimited size (cache size = memory size) – Any misses must be compulsory misses
  Simulate again with a fully associative cache of the intended size - Any new misses must be capacity misses
  Simulate a third time, with the actual intended cache - Any new misses must be conflict misses

## Slide 8: Review: Fixing cache misses
Compulsory misses
  First reference to a address
  No way to completely avoid these
  Reduce by increasing block size
  This reduces the total number of blocks
Capacity misses
  Would have a hit with a large enough cache
  Reduce by building a bigger cache
Conflict misses
  Would have had a hit with a fully associative cache
  Cache does not have enough associativity
  Reduce by increasing associativity

## Slide 9: 3 C’s Sample Problem
Consider a cache with the following configuraion: write-allocate, total size is 64 bytes, block size is 16 bytes, and 2-way associative. The memory address size is 16 bits and byte-addressable. The replacement policy is LRU. The cache is empty at the start.
For the following memory accesses, indicate whether the reference is a hit or miss, and the type of a miss (compulsory, conflict, capacity)

## Slide 10: Cache Parameters vs. Miss Rate
Cache Size
Block Size
Associativity
Replacement policy

## Slide 11: 3 C’s Sample Problem
Total size is 64 bytes, block size is 16 bytes, and 2-way associative:

## Slide 12: 3 C’s Practice Problem – 3 C’s
Address | Infinite | FA | SA | 3Cs
0x00 |  |  |  | 
0x14 |  |  |  | 
0x27 |  |  |  | 
0x08 |  |  |  | 
0x38 |  |  |  | 
0x4A |  |  |  | 
0x18 |  |  |  | 
0x27 |  |  |  | 
0x0F |  |  |  | 
0x40 |  |  |  | 

## Slide 13: 3 C’s Practice Problem – 3 C’s
Address | Infinite | FA | SA | 3Cs
0x00 | M | M | M | 
0x14 | M | M | M | 
0x27 | M | M | M | 
0x08 | H | H | H | 
0x38 |  |  |  | 
0x4A |  |  |  | 
0x18 |  |  |  | 
0x27 |  |  |  | 
0x0F |  |  |  | 
0x40 |  |  |  | 

## Slide 14: 3 C’s Practice Problem – 3 C’s
Address | Infinite | FA | SA | 3Cs
0x00 | M | M | M | Compulsory
0x14 | M | M | M | Compulsory
0x27 | M | M | M | Compulsory
0x08 | H | H | H | ---
0x38 |  |  |  | 
0x4A |  |  |  | 
0x18 |  |  |  | 
0x27 |  |  |  | 
0x0F |  |  |  | 
0x40 |  |  |  | 

## Slide 15: 3 C’s Practice Problem – 3 C’s
Address | Infinite | FA | SA | 3Cs
0x00 | M | M | M | Compulsory
0x14 | M | M | M | Compulsory
0x27 | M | M | M | Compulsory
0x08 | H | H | H | ---
0x38 | M | M | M | Compulsory
0x4A | M | M | M | Compulsory
0x18 | H | M | H | ---
0x27 | H | M | M | Capacity
0x0F |  |  |  | 
0x40 |  |  |  | 

## Slide 16: 3 C’s Practice Problem – 3 C’s
Address | Infinite | FA | SA | 3Cs
0x00 | M | M | M | Compulsory
0x14 | M | M | M | Compulsory
0x27 | M | M | M | Compulsory
0x08 | H | H | H | ---
0x38 | M | M | M | Compulsory
0x4A | M | M | M | Compulsory
0x18 | H | M | H | ---
0x27 | H | M | M | Capacity
0x0F | H | M | M | Capacity
0x40 | H | H | M | Conflict

## Slide 17: Cache Size
Cache size in the total data (not including tag) capacity
  bigger can exploit temporal locality better
  not ALWAYS better
Too large a cache adversely affects hit & miss latency
  smaller is faster => bigger is slower
  access time may degrade critical path
Too small a cache
  doesn’t exploit temporal locality well
  useful data replaced often
Working set: the whole set of data executing application references
  Within a time interval
hit rate
cache size
“working set”
size

## Slide 18: Block size (also called Line size)
Block size is the data that is associated with an address tag
  Sub-blocking: A block divided into multiple pieces (each with V bit)
    Can improve “write” performance
Too small blocks
  don’t exploit spatial locality well
  have larger tag overhead
Too large blocks
  too few total # of blocks
    likely-useless data transferred
    Extra bandwidth/energy consumed
Block size
hit rate

## Slide 19: Associativity
How many blocks can map to the same index (or set)?
Larger associativity
  lower miss rate, less variation among programs
  diminishing returns
Smaller associativity
  lower cost
  faster hit time
    Especially important for L1 caches
Power of 2 associativity?
associativity
hit rate

## Slide 20: Review: Fully-associative caches
tag data
tag
block offset
Address:
1 bit
3 bits
A block can go
to any location
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Memory
100
120
140
170
190
210
230
250

## Slide 21: Review: Direct-mapped caches
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
tag data
78
120
71
173
21
28
200
225
tag
line index
block offset
Address:
0
1
2
3
1 bit
2 bits
1 bit
Cache
Memory
A block can go
to one location

## Slide 22: Review: Set-associative cache
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
tag data
78
120
71
173
21
28
200
225
tag
set index
block offset
Address:
Set 0
Set 1
1 bit
1 bits
2 bit
Way0
Way1
Memory

## Slide 23: All together
Fully associative
Direct mapped
Set associative

## Slide 24: Practice Problem 1: CPI with caches
The grinder application run on the LC2k with full data forwarding and all branches predicted not-taken has the following instruction frequencies:
45% R-type 20% Branches 15% Loads 20% Stores
In grinder, 40% of branches are taken and 50% of LWs are followed by an immediate use.
The I-cache has a miss rate of 3% and the D-cache has a miss rate of 6% (no overlapping of misses). On a miss, the main memory is accessed and has a latency of 100 ns. The clock frequency is 500 MHz.
What is the CPI of grinder on the LC2k?

## Slide 25: Practice Problem 1: Solution
The grinder application run on the LC2k with full data forwarding and all branches predicted not-taken has the following instruction frequencies:
45% R-type 20% Branches 15% Loads 20% Stores
In grinder, 40% of branches are taken and 50% of LWs are followed by an immediate use.
The I-cache has a miss rate of 3% and the D-cache has a miss rate of 6% (no overlapping of misses). On a miss, the main memory is accessed and has a latency of 100 ns. The clock frequency is 500 MHz.
What is the CPI of grinder on the LC2k?
Stalls per cache miss = 100 ns / 2ns = 50 cycles (500 Mhz ➜ 2ns cycle time)
CPI = 1 + data hazard stalls + control hazard stalls + icache stalls + dcache stalls
CPI = 1 + 0.15*0.50*1 + 0.20*0.40*3 + 1*0.03*50 + 0.35*0.06*50

## Slide 26: Practice Problem 2: Memory Usage
Say you have the following:
  A program that generates 2 Billion loads and 1 Billion stores, each 4 bytes in size.
  A cache with a 32-byte block which gets a 95% hit rate on that program.
How many bytes of memory would be read and written if:
  We had a write-though cache with a no-write allocate policy?
  We had a write-back cache with a write-allocate policy? (Assume 25% of all misses result in a dirty eviction)
  We had no cache?

## Slide 27: Practice Problem 2: Solution (1/3)
Let’s start with the no-cache case.
  All stores go to memory and are 4 bytes each
    Writes: 1 billion stores* 4 bytes = 4 billion bytes
  All loads go to memory and are 4 bytes each.
    Reads: 2 billion loads* 4 bytes = 8 billion bytes
Write-though, no allocate.
  All stores still go to memory and are still 4 bytes each.
    Writes: 1 billion stores* 4 bytes = 4 billion bytes
  Only loads that miss in the cache go to memory. But they read the full cache block.
    Reads: 2 billion loads* 0.05* 32 bytes = 3.2 billion bytes

## Slide 28: Practice Problem 2: Solution (2/3)
Write-back, write-allocate (data reads)
  Store misses result in a cache block being read.
    Reads: 1 billion stores* 0.05* 32 bytes = 1.6 billion bytes
  Load misses result in a cache block being read.
    Reads: 2 billion loads* 0.05* 32 bytes = 3.2 billion bytes
  So that is 4.8 billion bytes of data read.

## Slide 29: Practice Problem 2: Solution (3/3)
When do we write to memory?
  Only on dirty evictions. Can be done by both loads and stores.
    Recall we are assuming 25% of all evictions are of dirty data.
Write-back, write-allocate (data writes)
  Store misses result in dirty eviction 1/4 of the time.
    Reads: 1 billion stores* 0.05* 32 bytes*(.25) = 0.4 billion bytes
  Load misses result in a cache block being read.
    Reads: 2 billion loads* 0.05* 32 bytes*(.25) = 0.8 billion bytes
Note: could have just taken the read numbers and multiplied by 25%.

## Slide 30: Practice Problem 3: CPI w/ Caches 2
Given a 200 MHz processor with 8KB instruction and data caches and a with memory access latency of 20 cycles. Both caches are 2-way associative. A program running on this processor has a 95% icache hit rate and a 90% dcache hit rate. On average, 30% of the instructions are loads or stores. The CPI of this system, if caches were ideal would be 1.
Suppose you have 2 options for the next generation processor, which do you pick?
  Option 1: Double the clock frequency—assume this will increase your memory latency to 40 cycles. Also assume a base CPI of 1 can still be achieved after this change.
  Option 2: Double the size of your caches, this will increase the instruction cache hit rate to 98% and the data cache hit rate to 95%. Assume the hit latency is still 1 cycle.

## Slide 31: Practice Problem 3: Solution
Option 1: (double clock freq, base cycle time is 5 ns, so new cycle time is 2.5 ns)
  CPI = baseCPI + IcacheStallCPI + DcacheStallCPI CPI = 1.0 + 0.05*40 + 0.3*0.1*40 = 4.2
Execution time = 4.2 * Ninstrs * 2.5ns = 10.5ns * Ninstrs
Option 2 (icache/dcache miss rates lowered to 2% and 5%)
  CPI = baseCPI + IcacheStallCPI + DcacheStallCPI CPI = 1.0 + 0.02*20 + 0.3*0.05*20 = 1.7
Execution time = 1.7 * Ninstrs * 5ns = 8.5ns * Ninstrs
Therefore, Option 2 is the better choice

## Slide 32: Practice Problem 4: Guess that cache!
Block size: ?
Associativity: ?
Number of sets: ?
Here is the series of address references (in hex) to a cache of size 512 bytes. You are asked to determine the configuration of the cache. Assume 12-bit addresses
0x310 – Miss
0x30f – Miss
0x510 – Miss
0x31f – Hit
0x72d – Miss
0x72f – Hit
0x320 – Miss
0x520 – Miss
0x720 - Miss

## Slide 33: Practice Problem 4: Solution
Here is the series of address references (in hex) to a cache of size 512 bytes. You are asked to determine the configuration of the cache. Assume 12-bit addresses
0x310 – Miss
0x30f – Miss
0x510 – Miss
0x31f – Hit
0x72d – Miss
0x72f – Hit
0x320 – Miss
0x520 – Miss
0x720 - Miss
Determine block size
First hit must be brought in by another miss
Take closest address: 0x310, so know block size must be at least 16 bytes so 0x31f brought in when 0x310 miss occurs
Now, is the block size larger? Know that 0x30f was a miss, thus 0x310 and 0x30f not in the same block. Thus, block size must be <= 16 bytes
Thus Block Size = 16 bytes

## Slide 34: Practice Problem 4 : Solution (2)
Here is the series of address references (in hex) to a cache of size 512 bytes. You are asked to determine the configuration of the cache. Assume 12-bit addresses
0x310 – Miss
0x30f – Miss
0x510 – Miss
0x31f – Hit
0x72d – Miss
0x72f – Hit
0x320 – Miss
0x520 – Miss
0x720 - Miss
Determine associativity
Assume direct mapped: 3-bit tag, 5-bit index, 4-bit offset.
If direct mapped 0x310 and 0x510 would both map to index 9,
Thus 0x31f could not be a hit. So, not direct mapped.
Assume 2-way associative: 4-bit tag, 4-bit index, 4-bit offset
This fixes the green accesses, and allows 0x31f to be a hit.
What about > 2-way associative?
Now we also know that 0x720 is a miss even though 3 accesses
earlier 0x72f was a hit, and thus it is in the cache. The intervening 2 accesses must kick it out, 0x320 and 0x520. Both go to set 2. If the associativity was > 2, then 0x720 would be a hit. So, must conclude that cache is 2-way associative.
Lastly, number of sets = 512 / (2 * 16) = 16