## Slide 1: 24. Virtual Memory: Design and Speed

## Slide 2
Next topic: Placing Caches in a VM System
VM systems give us two different addresses: virtual and physical
Which address should we use to access the data cache?
  Physical address (after VM translations).
    We have to wait for the translation; slower.
  Virtual address (before VM translation).
    Faster access.
    More complex.
2
EECS 370: Introduction to Computer Organization
Poll: Which would be faster?
Address cache with virtual address
Address cache with physical address

## Slide 3: Cache & VM Organization: Option 1
Physically-addressed Cache
Low complexity
Slower
TLB
cache
VA
PA
CPU
miss
hit
memory
virtual address
page table

## Slide 4
EECS 370: Introduction to Computer Organization
Physically addressed caches
Perform TLB lookup before cache tag comparison
  Use bits from physical address to access cache (tag, set index, and block offset bits)
Slower access?
  Tag lookup takes place after the TLB lookup
Simplifies some VM management
  When switching processes, TLB must be invalidated, but cache OK to stay as is
  Implications? Might result in fewer cache misses if context switches very common (but they generally are not)
4

## Slide 5
Page offset
Virtual page number
Virtual address
tag
Physical Page Number
tag
tag
tag
Page offset
Physical Page Number
Physical Page Number
Physical Page Number
Physical Page Number
Physically addressed caches
Physical address
Step 1: Virtual address to Physical
TLB
Set Index
Tag
Block offset
Set1 tag
Set1 tag
Set0 tag
Set0 tag
Set2 tag
Set2 tag
tag
comp
tag
comp
Cache
Step 2: Access the cache with
physical address obtained from
translation
2-way set associative cache

## Slide 6: Physically addressed caches: detailed flow
data to processor
TLB
cache
VA
PA
CPU
page table
miss
hit
~ 1 cycle
1-10s cycles
1 to 100s cycles
(cached or not)
virtual address
memory
miss
hit
100s cycles
valid page (update TLB)
invalid page
disk
1,000,000s cycles
bring in page (update memory, page table & TLB)

## Slide 7: Cache & VM Organization: option 2
Virtually-addressed Cache
Faster
High complexity (aliasing)
TLB
VA
PA
CPU
miss
hit
memory
virtual address
page table
cache

## Slide 8
tag
set index
block offset
TLB is accessed in parallel with cache lookup.
Physical address is used to access main memory in case of a cache miss.
Set1 tag
Set1 tag
Set0 tag
Set0 tag
Set2 tag
Set2 tag
Virtual address
tag
comp
tag
comp
Virtually addressed caches
2-way set associative cache

## Slide 9: Virtually addressed caches: detailed flow
data to processor
TLB
cache
VA
PA
CPU
page table
miss
hit
~ 1 cycle
1-10s cycles
1 to 100s cycles
(cached or not)
virtual address
memory
hit
100s cycles
valid page (update TLB)
invalid page
disk
1,000,000s cycles
bring in page (update memory, page table & TLB)
miss
(update cache)

## Slide 10
Cache uses bits from the virtual address to access cache (tag, set index, and block offset)
Perform the TLB only if the cache gets a miss.
Problems:
  Aliasing: Two processes may refer to the same physical location with different virtual addresses (synonyms)
  Two processes may have same virtual addresses with different physical addresses (homonyms)
  When switching processes, TLB must be invalidated, dirty cache blocks must be written back to memory, and cache must be invalidated to solve homonym problem
Virtually addressed caches

## Slide 11
It must be able to modify the page table register, update page table values, etc.
To enable the OS to do this, BUT not the user program, we have different execution modes for a process.
  Executive (or supervisor or kernel level) permissions and
  User level permissions.
OS Support for Virtual Memory

## Slide 12: References (not part of Course Syllabus)
See how Intel’s memory management hardware works, Intel x86 Software Manual: http://www.intel.com/content/www/us/en/architecture-and-technology/64-ia-32-architectures-software-developer-vol-3a-part-1-manual.html
  Chapter 4 is on Paging
Linux page table management: https://www.kernel.org/doc/gorman/html/understand/understand006.html

## Slide 13: Now you are a Computer Architect (yay!)
One architecture, many micro architecture
Caching, utilization, speculation
If you like this stuff, take EECS 470, 482
Study for the final & have a fun (and safe) summer!
Hope you can drop by when we're back in person?
"Leading a student to learning's treasures Gives a teacher untold pleasures!"